## Slide 1: WF on symbol interleaver for NR
Qualcomm, Ericsson , Interdigital
3GPP TSG-RAN WG1 #88
Athens, Greece, 13th – 17th February 2017
Agenda: 8.1.2.1.1
R1-1704098

## Slide 2: Background
NR shall support large bandwidth allocations.
CBs span limited frequency bandwidth and additional frequency diversity can be exploited to provide significant gains
  Each OFDM symbol may carry many CBs, especially in regimes of medium and high spectral efficiency
A frequency domain interleaver that allows the CB to span across the whole allocation has clear benefits
Agreements:
  For the DL/UL data channels, study whether/how the interleaving is performed in the codeword to layer mapping procedure (e.g., a per-OFDM-symbol subcarrier interleaver in the codeword to layer mapping procedure, etc.)
    This may or may not be connected with coding design

## Slide 3: Proposal
For the DL/UL data channels, NR supports an interleaver within an OFDM symbol
  This may or may not be connected with CW to layer mapping and/or coding design
  The design should consider low-latency receiver processing aspects and UE complexity aspects
  FFS: Details