## Slide 1: WF on UL Frequency Selectivity
Nokia, ASB, QualComm, CATT, [Samsung], [MediaTek]
3GPP TSG RAN WG1 Meeting #88 bis
Spokane, WA, USA, 3rd - 7th April, 2017
Agenda item: 8.1.2.1.4
R1-1706636

## Slide 2: Background
RAN1 NR ad hoc meeting in January 2017 has this agreement:
Support at least the following UL transmission schemes for data in NR
  Scheme A: Codebook based UL transmission
    Support frequency selective precoding for CP-OFDM when the number of transmission port is greater than X (FFS: Value of X).
    Study codebook design including single-stage and multi-stage, e.g., W1W2 structure, codebook
    Study the following DL signaling, e.g.,
      One level DCI
      Two level DCI
      MAC CE
      DCI associated with PDSCH (like UCI associated with PUSCH in LTE)
  Scheme B: Non-codebook based UL transmission
    Support frequency selective precoding for CP-OFDM when the number of transmission port is greater than Y (FFS: Value of Y).
    Support the indication of DL measurement RS for UE to calculate candidate precoder
    Study the mechanisms for UL precoder determination, e.g. precoded SRS based, non-precoded SRS based, hybrid precoded and non-precoded SRS based
  Diversity-based transmission schemes
    FFS: Whether the scheme has specification impact or not
  FFS: Merging of the schemes

## Slide 3: Background
RAN1 NR #88 meeting in February 2017 has this agreement:
Agreements:
Scheme A: Codebook based UL transmission
  For the previous agreement “Support frequency selective precoding for CP-OFDM when the number of transmission port(s) is equal to or greater than X (FFS: Value of X).”, FFS the value X and the interpretation of transmission port(s)
Scheme B: Non-codebook based UL transmission
  For the previous agreement “Support frequency selective precoding for CP-OFDM when the number of transmission port(s) is equal to or greater than Y (FFS: Value of Y).”, FFS the value Y and the interpretation of transmission port(s)

## Slide 4: Proposal
For CP-OFDM, both Scheme A (codebook based UL) and Scheme B (non-codebook based UL) support frequency selective precoding when
  the number of PUSCH port (X) is greater than 4
FFS: support frequency selective precoding when X=4
FFS: support frequency selective precoding when X=2