## Slide 1: WF on Criterion for Selection of CRC length
Ericsson
R1-1709272
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China ,15th - 19th May 2017
Agenda item 7.1.4.1.1.1

## Slide 2: Background (1)
Agreement (RAN1 NR AdHoc):
Before code block segmentation, LTB,CRC bit TB-level CRC are attached to the end of the transport block
  LTB,CRC <=24 bits
  LTB,CRC value is determined to satisfy probability of misdetection of TB error <=10-6
Inherent error detection of LDPC codes is taken into account in determining the LTB,CRC value

## Slide 3: Background (2)
Agreement: (RAN1#88bis)
  Number of bits for TB-level CRC is: LTB,CRC =24 bits, at least for TBs larger than a threshold (e.g. around 512 bits)
  FFS the value of LTB,CRC for TBs smaller than the threshold, and the value of the threshold (0 is not precluded)
  If a TB is segmented into 2 or more CBs after code block (CB) segmentation,
    CB-level CRC is applied, i.e., CRC bits are attached to each code block individually (as in LTE)
    Number bits for CB-level CRC is: 0 < LCB,CRC <= 24 bits
      Exact value(s) LCB,CRC are to be agreed after base graph(s) are agreed, taking into account inherent LDPC PC capability
  FFS whether for a code block group (CBG) containing 2 or more CBs but not all CBs of the TB, any additional CRC bits are attached to the CBG
    To be decide after decision on the value(s) of LCB,CRC

## Slide 4: Discussion
In the agreement, it is not specified how the probability of miss detection is defined
For blind detection situations (e.g. control), FAR is measured for random input
In a situation where actual codewords are transmitted, probability of undetected error ( is a better measure (see next slide)

## Slide 5: FAR vs. Pud
Pud= FAR x BLER
Pud is important from a system level perspective
  Takes into account the probability that an error actually occurs

## Slide 6: Proposal:
Pud is used as selection criterion for the number of CRC bits to attach. For both
  Value of LTB,CRC for TBs smaller than the threshold
  Value of LCB,CRC for CB-level CRC bits
For TBs smaller than the threshold, LTB,CRC value is determined to satisfy probability of undetected TB error: Pud,TB <=10-6