## Slide 1: WF on TB-level CRC reduction for small size TBs
3GPP TSG RAN1 #89 meeting
Hangzhou, P.R. China 15th - 19th May 2017
Agenda Item: 7.1.4.1.1.1
LG Electronics, KT, Nokia, ASB
R1-1709281

## Slide 2
Agreement at #88b meeting
  Number of bits for TB-level CRC is: LTB,CRC =24 bits, at least for TBs larger than a threshold (e.g. around 512 bits)
  FFS the value of LTB,CRC for TBs smaller than the threshold, and the value of the threshold (0 is not precluded)
TBS table of 3GPP LTE
Background
1/5 code rate
Minimum code rate of base graph #2
1/3 code rate
Minimum code rate of base graph #1
2/3 code rate
Maximum code rate of base graph #2
8/9 code rate
Maximum code rate of base graph #1
The minimum TB size is changed according to code rate

## Slide 3
FAR (or undetected error prob.) is changed according to code rate (R) and information size (K)
  FAR decreases as TB size increases.
  FAR increases as code rate increases.
It is not straightforward whether the FAR of 2/3 code rate with 136 TB size is worse than the FAR of 1/5 code rate with 32 TB size or not.
Background
Not used at the LTE TBS table
TB size
The minimum TB sizes of different code rates have a similar FAR (or undetected error prob.)
The values of FAR are obtained by using LG’s LDPC code

## Slide 4
After the minimum TB size for each code rate (or MCS index) and base graph(s) are agreed, the exact bit size(s) of TB-level CRC for TBs smaller than threshold(s) should be agreed.
  At least following sets of code rate and TB size should be considered
    8/9 and 2/3 are respectively the maximum code rates of base matrix 1 and (nested) base matrix 2.
    1/3 and 1/5 respectively have the minimum TB sizes of base matrix 1 and (nested) base matrix 2.
Proposal