## Slide 1: WF on rate matching for Polar codes
Qualcomm, Ericsson, Intel, DoCoMo, LG Electronics, ZTE
3GPP TSG RAN WG1 #89 R1-1709362
May 15th – 19th 2017
Hangzhou, China
Agenda item: 7.1.4.2.1.2

## Slide 2: Background
Puncture (Type I puncture), shortening (Type II puncture) and repetition can provide the good trade off between performance and complexity
Before evaluating the performance for variable patterns for puncture, shortening and repetition, we need decide the power 2 integer for coded block size N

## Slide 3: Proposal (1/2)
Let M be supported # bits in allocated resource
K is payload size
Let NDM Minimum power of 2 >=M
NM is determined by
  NDM M >= β* NMM /2 β in [1, 2]
  NDM /2 M < β* NMM /2 and K/M < Rrepthr
  FFS the value of β and Rrepthr
NR minimum power 2 >= K/Rmin
  Rmin is the supported minimum coding rate
  FFS the value of the supported Rmin
Nmax power of 2 maximum supported coded block size
Determine the coded block size N as min(NM, NR, Nmax)

## Slide 4: Proposal (2/2)
Repetition is applied when M > N
Puncture or shortening is applied when M < N
  Puncture for rate <= Rpsthr
  Shortening for rate > Rpsthr
  FFS the value of Rpsthr