## Slide 1: WF on Number of symbols for SRS
Ericsson, Sony, Mitsubishi Electric, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.2.4.4
R1-1709378

## Slide 2: Previous Agreements
Agreements:
A UE can be configured with an X-port SRS resource, where the SRS resource spans one or multiple OFDM symbols within a single slot
  FFS where all of the X SRS ports are sounded in each OFDM symbol
FFS at least for the purposes of CSI acquisition:
  FFS a multi-symbol SRS resource can be configured such that the X SRS ports in each OFDM symbol are transmitted in different locations of the band in different OFDM symbols in the slot in a frequency hopping manner
    Note: This allows sounding a larger part of (or the full) UE bandwidth using narrower band SRS transmissions
    Note: at any OFDM symbol, all X ports are sounded in the same portion of the band
  Note: Consider UE RF implementation aspects on SRS design that may place constraints on the design of the symbol-wise hopping pattern
    e.g., Required time for frequency re-tuning (if re-tuning needed) or transient period if re-tuning is not needed

## Slide 3: Proposal
NR supports configuration of an X-port SRS resource spanning N OFDM symbols within the same slot where
  N = 1, 2, 4 at least