## Slide 1: WF on Discovery Enhancements for Bandwidth Limited Remote UEs
Intel, Sony
3GPP TSG RAN WG1 Meeting #89 R1-1709400
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item - 6.2.9.2.2

## Slide 2: Background
Bandwidth limited devices cannot process the whole PSDCH bandwidth and thus existing discovery process can take long time and even may be power inefficient
Additional enhancement to the discovery process may be necessary for bandwidth limited wearable/MTC devices

## Slide 3: Proposal
Discovery enhancements for bandwidth limited Remote UEs are beneficial
The following design enhancements are further studied
  For Model A discovery,
    Multi-shot discovery transmission across bandwidth of discovery pool(s)
  For Model B discovery,
    eNB assistance signaling, e.g. eNB signaling of Model B discovery response message
    Response message is transmitted within associated Remote UE monitoring bandwidth (e.g. in the same sub-channel as solicitation message or other associated discovery resource). Details are FFS
Other design options are not precluded