## Slide 1
3GPP TSG RAN WG1 Meeting #89 R1-1709441
Hangzhou, China, 15-19 May 2017
Agenda item: 7.1.1.2.1
WF on PBCH DMRS Design
Huawei, HiSilicon, …

## Slide 2: Background
Working assumption in RAN1#88bis:
For NR-PBCH transmission, NR supports a single antenna port based transmission scheme only.
  FFS: Same or different antenna port(s) are defined for NR-PSS, NR-SSS and NR-PBCH within an SS block
  Companies are encouraged to further evaluate NR-PBCH performance
The following agreements for PBCH were achieved in RAN1#88bis
Time index indication: PBCH conditioned that mobility and HO related requirements can be met
  Note: RAN1 assumes that RAN2 will check against to RAN2 requirements
PBCH BW: 288 subcarriers, 2 OFDM symbols (additional symbols if MIB size larger than assumed)
PBCH phase reference: DMRS

## Slide 3: Proposal
Confirm working assumption on antenna port for NR-PBCH in RAN1#88bis
  For NR-PBCH transmission, NR supports a single antenna port based transmission scheme only
Same antenna port is defined for NR-PSS, NR-SSS and NR-PBCH within an SS block
  Note: NR-SSS can be used for NR-PBCH demodulation
For PBCH DMRS mapping, the following should be supported
  PBCH DMRS is mapped into the PRBs with PSS/SSS and the ones without PSS/SSS with different density in both frequency and time domains
  PBCH DMRS is mapped into two OFDM symbols of each SS block in time domain
    FFS: the number of PBCH symbols into which PBCH DMRS is mapped
For PBCH DMRS sequence generation, the following should be supported,
  PBCH DMRS sequence is generated based on Cell ID only