## Slide 1: WF on DL DMRS multiplexing in the time domain
3GPP TSG RAN WG1 Meeting #89 R1-1709477
Hangzhou, China, 15th – 19th May, 2017
Agenda Item: 7.1.2.4.2
ZTE, Qualcomm

## Slide 2: Background
Conclusions in RAN1#88bis:
Continue discussions/evaluations until the next meeting about following DMRS port multiplexing schemes for 2 adjacent front-loaded DMRS symbols in the time domain, and RAN1 will definitely conclude this down selection in the next meeting
  Alt. 1: OCC
  Alt. 2: TDM
  Alt. 3: Frequency domain multiplexing only with the time domain repetition/ with a pattern shift
  Alt. 4: Configure between Alt. 1 and Alt. 2
    Consider phase noise impact in the high frequency band
  Alt. 5: Configure between Alt. 1 and Alt. 3
Notes: i

## Slide 3: Proposal
  For DMRS port multiplexing schemes on 2 adjacent front-loaded DMRS symbols in the time domain:
    Alternative 1: Support DMRS configurations with two alternatives
      Time domain OCC (TD-OCC) of antenna ports is supported. In addition, for the other alternative only one of following is supported:
        Case 1A: TDM of antenna ports
        Case 1B: Time domain repetition of all antenna ports
    Alternative 2: Support DMRS configurations with one alternative:
      Case 2A: TDM of antenna ports
      Case 2B: Time domain repetition of antenna ports
      Case 2C: TD-OCC of antenna ports
    Notes:
      This is for both SU-MIMO and MU-MIMO
      If 1B or 2B is chosen then whether and/or not pattern shift is used must be decided
  Alternative 1 supported by: Ericsson, Nokia, ASB, ZTE, Qualcomm, NTT DOCOMO,
  Alternative 2 supported by: Samsung
Notes: i