## Slide 1: WF on reporting UE capability of beam correspondence
Samsung, Intel
3GPP TSG RAN WG1 Meeting #NR 89 R1-1709494
Hangzhou, China, 15th - 19th May 2017
Agenda item 7.1.1.4.2

## Slide 2: Background
Agreements:
Support capability indication of UE beam correspondence related information to TRP
  FFS details including capability definition, case(s) (if any) when the indication is not necessary
Agreements:
For the definition of beam correspondence:
  Confirm the previous working assumption of the definition
    Note: this definition/terminology is for convenience of discussion
  The detailed performance conditions are up to RAN4
Working assumption:
The followings are defined as Tx/Rx beam correspondence at TRP and UE :
  Tx/Rx beam correspondence at TRP holds if at least one of the following is satisfied:
    TRP is able to determine a TRP Rx beam for the uplink reception based on UE’s downlink measurement on TRP’s one or more Tx beams.
    TRP is able to determine a TRP Tx beam for the downlink transmission based on TRP’s uplink measurement on TRP’s one or more Rx beams
  Tx/Rx beam correspondence at UE holds if at least one of the following is satisfied:
    UE is able to determine a UE Tx beam for the uplink transmission based on UE’s downlink measurement on UE’s one or more Rx beams.
    UE is able to determine a UE Rx beam for the downlink reception based on TRP’s indication based on uplink measurement on UE’s one or more Tx beams.
  More refined definition can still be discussed

## Slide 3: Proposal
  NR supports to report UE capability of beam correspondence by RACH procedure, e.g., via Msg. 3.