## Slide 1: WF on Carrier Selection in PC5 operation
LG Electronics, ZTE
3GPP TSG RAN WG1 Meeting #89 R1-170xxxx
Hangzhou, China 15th – 19th May 2017
Agenda item: 6.2.3.1.1

## Slide 2: Background
Objective of new WID on 3GPP V2X Phase (RP-170798)
  Specify solutions for the following PC5 functionalities, which can co-exist in the same resource pools as Rel-14 functionality and use the same scheduling assignment format (which can be decoded by Rel-14 UEs), without causing significant degradation to Rel-14 PC5 operation compared to that of Rel-14 UEs:
    Carrier aggregation (up to 8 PC5 carriers);
    64QAM;
    Reduce the maximum time between packet arrival at Layer 1 and resource selected for transmission;
    Radio resource pool sharing between UEs using mode 3 and UEs using mode 4;

## Slide 3: Proposals
  The UE selects a set of PC5 carrier(s) used for the actual transmission at least based on CBR measured by Rel-14 procedure.
  FFS other criteria
  FFS the time scale of TX carrier set selection
  This selection applies at least when the number of supported TX carriers is smaller than the number of supported RX carriers.
    FFS for other cases