## Slide 1: WF on interference randomization for NB-IoT
Qualcomm, Huawei, HiSilicon, Ericsson
R1-1709563
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th - 19th May 2017
Agenda item 6.1.6

## Slide 2: Background
In [1,2] performance degradation was observed for NPBCH and NB-SIB1 in interference limited scenarios.
  These issues were solved for Rel-13 in [3,4]
Similar issues are present for NPDSCH and NPDCCH in the more general case [5]
References:
  [1] R1-1702514 “Discussion on performance issues for PBCH and SIB1 in interference-limited scenarios”
  [2] R1-1703087 “Motivation for change to scrambling of NB-IoT MIB/SIB transmission”
  [3] R1-1703964 “NPBCH symbol rotation for interference randomization in NB-IoT
  [4] R1-1703913 “Correction on the scrambling of NPDSCH carrying the BCCH”
  [5] R1-1708756 “Interference randomization for Rel-14 NB-IoT”

## Slide 3: Proposal
An interference randomization scheme based on rotated IQ symbols (similar to the one of NPBCH) is introduced in Rel-14:
  For NPDCCH:
    For Type-2 and Type1-CSS in non-anchor carriers
    For Type-1A and Type-2A CSS
    [For USS, based on RRC configuration]
  For NPDSCH:
    For NPDSCH scrambled by RA-RNTI, TC-RNTI and P-RNTI in non-anchor carriers
    For G-RNTI
    [For NPDSCH scrambled by C-RNTI, based on RRC configuration]
  FFS details of the sequence initialization c_init.
For NPUSCH in Rel-14:
  In msg3 in non-anchor carrier, change the scrambling sequence initialization to a non-linear combination of cell ID and slot/frame number
  [For NPUSCH scrambled with C-RNTI, change the scrambling sequence initialization to a non-linear combination of cell ID and slot/frame number based on RRC configuration]
  FFS details of the sequence initialization c_init