## Slide 1: WF on Simulation Assumptions for Backhaul Latency and Fixed UE Height
Nokia, Alcatel-Lucent Shanghai Bell, …
R1-1709697
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China, May 15th – 19th 2017
Agenda item: 6.2.8.2

## Slide 2: Background
The inter-site backhaul latency might be non-ideal in the realistic network deployment.
  The simulation assumptions in TR 36.874 for non-ideal backhaul
    {5, 50}ms mandatory, {2, 10, 30}ms optional.
  The simulation assumptions in TR 36.741 for non-ideal backhaul
    0ms, 2ms (optional), 5ms, 50ms.

## Slide 3: Background
The agreed simulation assumptions in RAN1#88bis for aerial-UE height are
  Uniformly distributed between 1.5 m and [150]m
  Optionally: fixed height values in the range between 1.5m and [150]m
  The agreed requirement for target UAV height in RAN2#98 meeting is up to 300m.

## Slide 4: Proposal
Proposal 1: Consider the backhaul link delay of 0ms, 5ms or 50ms in the simulation assumptions.
Proposal 2: Consider [50]m, [150]m, [200]m, [250]m and [300]m as the simulation assumptions for the cases with fixed aerial-UT height.