## Slide 1: Way Forward on bandwidth part for efficient wideband operation in NR
MediaTek, Huawei, HiSlicon
R1-1709736
3GPP TSG-RAN WG1 #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.7

## Slide 2: Proposals
Configuration of a DL bandwidth part further includes at least one CORESET
  Each CORESET consists of a set of PRBs spanning within the corresponding DL bandwidth part
  UE is expected to only monitor the CORESET in an active DL bandwidth part
  PDSCH in an active DL bandwidth part is scheduled by the PDCCH in the same DL bandwidth part
  PUSCH in an active UL bandwidth part is scheduled by the PDCCH in an active DL bandwidth part associated to the same UL bandwidth part
For the indication of active DL/UL bandwidth part(s) to a UE, the following options are considered
  Option #1: DCI
  Option #2: MAC CE
  Option #3: Time pattern (e.g. DRX like)