## Slide 1
WF on reciprocity based CSI acquisition
Huawei, HiSilicon, MediaTek, CATT, Softbank
3GPP TSG RAN WG1 Meeting #89 R1-1709768
Hangzhou, China 15 – 19 May 2017
Agenda item: 7.1.2.3.3

## Slide 2: Background
For the case of non-ideal channel reciprocity (e.g., less Tx ports than Rx ports at UE), study and evaluate at least the following candidate schemes
  Scheme 1 (Baseline for performance comparison): Non-PMI feedback
    Each company states the assumed scheme for non-PMI feedback
  Scheme 2: Partial CSI feedback for gNB to acquire full CSI
    Partial CSI is the information of the partial DL channel (e.g. partial DL channel vector/matrix or partial DL channel covariance matrix) with no reciprocal UL transmission due to the absence of Tx ports corresponding to the Rx ports at UE
  Scheme 3: CSI feedback with non-precoded/beamformed CSI-RS including CQI, RI and PMI
    For beamformed CSI-RS, precoding matrix is determined from CSI available at base station from SRS transmission
    PMI could be for a linear combination codebook
  Scheme 4: SRS switching
    SRS switching is used to obtain full channel information by multiple SRS transmission instants. Non-PMI CSI feedback can be used along with SRS switching
    Taking into account practical impairments in implementation (e.g., PLL accuracy, insertion loss, power imbalance, etc.)
  Scheme 5: Non-uniform beam sampling on codebook
    Configure different spatial resolutions in different spatial domain by CSR
  Combination of the above schemes can be considered
  Note: both performance and overhead should be considered when comparing the above schemes
Simulation parameters are provided on slide 4 of R1-1706809 with the following update
  Adding “2Tx2Rx” to “UE antenna configuration”
  Change “2GHz” to “4GHz” in “Carrier frequency”
  Companies describe the assumed UL-DL calibration model, striving for a common model

## Slide 3: Proposals
For the case of non-ideal channel reciprocity with less Tx ports than Rx ports at UE in TDD system, NR support at least one of the following alternatives:
  Alternative 1: combination of scheme 2 and scheme 3
  Alternative 2: scheme 3 only
  Alternative 3: scheme 4 only
  Note :The switching between different schemes can be dependent on rank or through RRC signaling configuration if more than one alternative are supported.

## Slide 4: Observations
Observation : With similar overhead, combination of scheme 2 and scheme 3 achieves significant performance gain over other schemes.
Chart: Gain{%}
| scheme 1 | combination of scheme 2 & scheme 3 | scheme 3 | scheme 4 | Upper bound
Average UPT gain | 0 | 40.54 | 16.69 | 24.84 | 53.75
5% UPT gain | 0 | 54.18 | 14.56 | 32.35 | 76.28

## Slide 5: Appendix
Parameters | Values
Duplex mode | TDD
Inter-BS distance | 200m
Carrier frequency | 4GHz
Simulation bandwidth | 10MHz
Channel model | UMi
BS Tx power | 41dBm
BS antenna configuration | (M, N, P, Mg, Ng) = (8, 8, 2, 1, 1); (dH,dV) = (0.8, 0.5)λ
BS TXRU mapping | (MTXRU, NTXRU, P, Mg, Ng) = (2, 4, 2, 1, 1)
UE antenna configurations | 2Rx, Cross-polarized with 0, 90deg
UE antenna height | Follow TR36.873
UE antenna gain | Follow TR36.873
UE receiver noise figure | 9 dB
Traffic model | Non-Full buffer, FTP model 1, 500KB packet size
UE distribution | 80% Indoor, 3km/h, 20% Outdoor, 30km/h
Scheduler | PF
HARQ scheme | CC with up to 3 retransmissions
UE receiver type | MMSE-IRC
Feedback assumption | Realistic
Channel estimation | Realistic
MIMO mode | MU-MIMO with rank adaptation, max rank =2
SRS hopping bandwidth | 4 PRB
SRS hopping period | 1 ms
Simulation assumption