## Slide 1: WF on UL Beam Management
Huawei, HiSilicon, Intel, Xinwei, MediaTek, InterDigital, […]
3GPP TSG RAN WG1 #89 | R1-17xxxxx
Hangzhou, China, May 15 – 19 2017 | Agenda Item: 7.1.2.2.1

## Slide 2: Background
Agreements in RAN1 88bis meeting:
  Confirm the WA from RAN1 AH1701 with the following update:
    NR supports at least one NW-controlled mechanism for beam management for UL transmission(s)
      FFS the details.
  Study whether or not the UE to provide information to gNB to assist UL beam management without UE beam correspondence
    E.g., the amount of SRS resources that is needed to train UE Tx beams, based on DL beam management results if available
  Study whether and how UE to use same transmission power for SRS transmission during one round of beam sweeping
    E.g., derived from beam-specific power control signalling and maximum transmit power
    FFS: spec. impact

## Slide 3: Proposal
Support UE to use same transmission power for SRS transmission during one round of beam sweeping
  FFS: details
    E.g., derived from beam-specific power control signalling and maximum transmit power
Support UE to provide information to gNB to assist UL beam management without UE beam correspondence
  FFS: details
    E.g., the amount of SRS resources that is needed to train UE Tx beams, based on DL beam management results if available
    E.g., gNB to derive the suitable amount of SRS resources for a UE based on PHR report
    E.g., the information can be semi-static or static e.g., integrated into UE beam correspondence state information by increasing UE beam correspondence state resolution via multi-bit string
Support UE to derive the UL beam sweeping behavior for SRS transmissions based on notification from gNB
  FFS: details
    E.g., information indicating whether UE should keep the same Tx beams or to use different Tx beams for SRS transmissions
    E.g., information indicating the number of SRS symbols and the number of SRS resources

## Slide 4: appendix

## Slide 5: Example
Notation
  Ng analog beams per level, Kg levels of beams
  NUE analog beams per level, KUE levels of beams
  Mg: UL Rx beam ambiguity at gNB conditioned on a selected DL gNB Tx beam
  MUE: UL Tx beam ambiguity at UE conditioned on a selected DL UE Rx beam
Hierarchical search type | Ng | NUE | Kg | KUE | Mg | MUE | # beam pair search attempt | Search overhead
Full search | 8 | 4 | 2 | 1 | N/A | N/A | 40 | 100%
Local search | N/A | N/A | N/A | N/A | 3 | 3 | 9 | 22.5%
Full search | 8 | 4 | 2 | 2 | N/A | N/A | 44 | 100%
Local search | N/A | N/A | N/A | N/A | 4 | 4 | 16 | 36%