## Slide 1: WF on Base Graph Selection for Small K and high R
Ericsson, LG,
R1-1714683
3GPP TSG RAN WG1 Meeting #90
Prague, P.R. Czechia 21th – 25th August 2017
Agenda item 6.1.4.1.6

## Slide 2: Background
Agreement: (RAN1 NR AdHoc #2)
  Base graph #1 is used for the initial transmission and subsequent re-transmissions of the same TB when
    CBS > X or code rate of the initial transmission > Y
  Base graph #2 is used for the initial transmission and subsequent re-transmissions of the same TB when
    CBS <= X and code rate of the initial transmission <= Y
  Working assumption : X = 2560 and Y = 0.67
  FFS after PCM decisions if X can be extended to 3840 and/or Y can be extended to 0.75

## Slide 3: Discussion (1)
Neither base graph #1 nor base graph #2 is optimized for K<512 AND R>2/3 since such combinations of block length and code rate are not so probable
If these combinations are needed, the best performing non-optimized base graph should be used

## Slide 4: Discussion (2)
The simulation results show that
  For K > ≈300 and R=3/4, base graph #1 performs better than base graph #2
  For K < ≈300 and R=3/4, base graph #2 performs better than base graph #1
The need for R>2/3 is more likely for K>300 than for K<300
Selecting one base graph to be used for all code rates R>2/3 is a simple solution

## Slide 5: Proposal
Use base graph #1 for all combinations of K<512 and R>2/3