## Slide 1: WF on pathloss offset of SUL for LTE-NR UL coexistence
Huawei, HiSilicon, MediaTek, China Telecom
3GPP TSG RAN WG1 meeting #90 R1- 1714835
Prague, Czech Republic, 21 – 25 August, 2017
Agenda item: 6.1.6

## Slide 2: Background
Conclusions: on RAN1#88b Study further at least the following issues when UL carrier in one frequency range and DL NR carrier in a different frequency range: Potential timing offset due to differences in channel delay profiles between UL and DL Pathloss difference between UL and DL (it is assumed that DL is used by a UE to measure the path loss)
Notes: Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.

## Slide 3: Background
Path loss differences between different carrier frequencies arise from path loss exponent, breakpoint, penetration loss, shadow fading, TX/RX antenna configuration including number of antennas, antenna gain, beamforming technologies.
R1-1709979

## Slide 4: Proposal
A pathloss offset and a threshold can be informed in the PRACH configuration corresponding to PRACH resources on the SUL frequency
  Whether pathloss offset is applied or not is according to the comparison between the threshold and UE’s PCell RSRP
FFS: Separate UE-specific pathloss offsets can be configured for power control of PUSCH/PUCCH/SRS.