## Slide 1: WF on Relay Assisted Resource Allocation for FeD2D
Intel, Sony, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #90 R1-1714847
Prague, Czech Republic, 21st – 25th August 2017
Agenda item - 5.2.9.2.3.2

## Slide 2: Background
Agreement from RAN1#88bis
  The following enhancements for sidelink unicast communication are studied further:
    eNB controlled resource allocation and configuration for communication between Relay and Remote UE
      eNB decision on resource allocation is relayed to Remote UE by Relay UE
    Relay UE assisted resource allocation and configuration under eNB control
    Remote UE assisted resource allocation
Agreement from RAN1#89
  Relay UE can control sidelink radio-resources used for transmission and reception by Remote UEs within sidelink resource pools which are configured by eNB
    FFS control signaling details

## Slide 3: Proposal
In Relay assisted resource allocation mode
  Remote UE is not expected to monitor all available sidelink communication resources within pools configured by eNB;
  Relay UE can use semi-static higher layer signaling to configure sidelink transmission and reception resources of Remote UEs;
    FFS control signaling details (pools, set of resources within pools, SPS configuration, etc.).
  Relay UE autonomously selects resource for sidelink transmission from preconfigured sidelink resource pools;
  Remote UE can be configured by Relay UE to autonomously select resource for sidelink transmission from the (pre)-configured set of sidelink resources or follow SCI grants provided by Relay UE;
  Relay UE can signal SCI grant to allocate specific resources for Remote UE transmission or activate/deactivate sidelink SPS configuration;
  Remote UE can request sidelink resources for communication. No new physical layer channel is introduced for scheduling request.