## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-1714867
Prague, Czech Republic, 21-25 August 2017
Agenda Item: 6.1.1.4.3
WF on power ramping and beam switching
Huawei, HiSilicon, NTT Docomo, LGE, …

## Slide 2: Background
In RAN1#89, the following agreement was achieved :
  If the UE conducts beam switching, the counter of power ramping remains unchanged
In RAN1#AH2, the following agreement was achieved :
  UE behavior when reaching the maximum power
    If the recalculated power is still at or above the Pc,max
      The UE can transmit at maximum power even if it changes its TX beam

## Slide 3: Background
Typical cases of UE beam switching for Msg1 retransmission
  UE without beam correspondence
  Better SS block is found
gNB can have the capability to control the balance between latency and interference
  When the load is low, UEs are allowed to do power ramping when the number of beam switching reaches a value.
  If UE wants to try all the candidate beams before power ramping when there is no beam correspondence, it is also allowed.
  Prevent for gNB to receive unexpected interference when UE changes Tx beam

## Slide 4: Proposal
If UE conducts beam switching and the number of beam switching in a power level has reached the gNB configured value, it is left to UE implementation whether the counter of power ramping remains unchanged or increases.
Configure the maximum count of continuously increasing power ramping in a certain beam, where,
  when the configured number is exceeded,
    UE should change its beam for PRACH preamble retransmission.