## Slide 1: WF on DL DMRS mapping
Huawei, HiSilicon, CATT, Spreadtrum, [Qualcomm]
3GPP TSG RAN WG1 NR Ad Hoc Meeting R1-1714883
Prague, Czech, 21-25 August 2017
Agenda item – 6.1.2.3.3

## Slide 2: Backgroud
In last meeting, there are following agreements:
Agreements:
The working assumption made in RAN1#89 for DM-RS is updated and agreed as follows for CP-OFDM:
A UE is configured by higher layers with DMRS pattern either from the front-loaded DMRS Configuration type 1 or from the front-loaded DMRS Configuration type 2 for DL/UL:
Configuration type 1:
One symbol:
  Comb 2 + 2 CS, up to 4 ports
Two symbols:
  Comb 2 + 2 CS + TD-OCC ({1 1} and {1 -1}), up to 8 ports
    Note: It should be possible to schedule up to 4 ports without using both {1,1} and {1,-1}.
Configuration type 2:
One symbol:
  2-FD-OCC across adjacent REs in the frequency domain, up to 6 ports
Two symbols:
    2-FD-OCC across adjacent REs in the frequency domain + TD-OCC (both {1,1} and {1,-1}) up to 12 ports
      Note: It should be possible to schedule up to 6 ports without using both {1,1} and {1,-1}.
From UE perspective, frequency domain CDMed DMRS ports are QCLed.
FFS: Whether the front-load DMRS configuration type for a UE for UL and DL can be different or not.
Note: If there are significant complexity/performance issues involved in the above agreements, down-selection can still be discussed

## Slide 3: Proposal-1
For the agreement: From UE perspective, frequency domain CDMed DMRS ports are QCLed. one clarification is that:
If DMRS pattern with two symbols, the CDMed DMRS ports are QCLed.
Example: CDMed port 0/1/6/9 is QCLed

## Slide 4: Proposal-2
Support the following DMRS port mappings for 1 symbol case:
For DMRS configuration type 1
2. And DMRS configuration type 2
Port indexing | Frequency offset: delta | FD-OCC: wf(0), wf(1) | 
XX0 | 0 | +1 | +1
XX1 | 0 | +1 | -1
XX2 | 1 | +1 | +1
XX3 | 1 | +1 | -1
Port indexing | Frequency offset: delta | FD-OCC: wf(0), wf(1) | 
XX0 | 0 | +1 | +1
XX1 | 0 | +1 | -1
XX2 | 2 | +1 | +1
XX3 | 2 | +1 | -1
XX4 | 4 | +1 | +1
XX5 | 4 | +1 | -1

## Slide 5: Illustrations for proposal-2
DMRS port mappings for 1 symbol case:
DMRS port mapping for configuration type-2
DMRS port mapping for configuration type-1