## Slide 1: WF on Fast Fading Modelling in UMa-AV
Nokia, Nokia Shanghai Bell
R1-1714899
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21th – 25th August 2017
Agenda Item: 5.2.8.3

## Slide 2
Background: Scenario
1000m
780m
Ray tracing in UMa-AV scenario: Ray tracing simulations at 2GHz frequency were performed using Aalborg, Denmark 3D map in a 1000m x 780m area.
BS antenna height is 25m, above roof top of nearby buildings.
Outdoor UEs are dropped with the height of 30m, 50, 75m, 100m, 200m, 300m.

## Slide 3
Background: Statistical modeling of LSPs
From ray tracing data, angular spreads in azimuth and elevation domains (ASD, ASA, ZSD, ZSA), delay spread, and Rician K factor are computed for all links
Following the methodology of TR38.901, the mean and standard deviation of log10(ASD), log10(ASA), log10(ZSD), log10(ZSA), log10(DS), K are calculated for each UE height
Fit the mean of these parameters with a quadratic function and compute the overall standard deviation
With the fit parameters, ASA, ASD, ZSA, ZSD, DS can be generated assuming log-normal distribution and K can be generated assuming normal distribution for any desired UAV UE height

## Slide 4
Background: ASD and ASA for LOS

## Slide 5
Background: ZSD and ZSA for LOS

## Slide 6
Background: DS and K for LOS

## Slide 7
Background: Height dependent LSP parameterization for LOS
LSP |  |  |  | 
Log10(ASD) | -0.96 | 2.54 | -0.45 | 0.38
Log10(ASA) | 0.00 | -1.74 | 3.43 | 0.31
Log10(ZSD) | 0.55 | -1.59 | 1.58 | 0.35
Log10(ZSA) | 0.34 | -1.92 | 2.42 | 0.30
Log10(DS) | 0.21 | -2.02 | 4.93 | 0.29
K | -13.43 | 62.81 | -56.30 | 5.76
Log10(ASD) | -0.96 | 2.54 | -0.45 | 0.38
Log10(ASA) | 0.00 | -1.74 | 3.43 | 0.31
Log10(ZSD) | 0.55 | -1.59 | 1.58 | 0.35
Log10(ZSA) | 0.34 | -1.92 | 2.42 | 0.30
Log10(DS) | 0.21 | -2.02 | 4.93 | 0.29
K | -13.43 | 62.81 | -56.30 | 5.76
In the table, the mean of a LSP parameter is fit with a quadratic equation
where with being the UE height in m.
The LSP is modeled as a normal distribution with mean and standard deviation ,

## Slide 8
Background: ASD and ASA for NLOS

## Slide 9
Background: ZSD and ZSA for NLOS

## Slide 10
Background: DS for NLOS

## Slide 11
Background: Height dependent LSP parameterization for NLOS
LSP |  |  |  | 
Log10(ASD) | -3.22 | 11.01 | -7.76 | 0.38
Log10(ASA) | -4.73 | 15.02 | -10.51 | 0.27
Log10(ZSD) | -5.61 | 20.72 | -18.39 | 0.52
Log10(ZSA) | -5.11 | 17.04 | -14.05 | 0.24
Log10(DS) | -4.89 | 16.30 | -10.60 | 0.26
Log10(ASD) | -3.22 | 11.01 | -7.76 | 0.38
Log10(ASA) | -4.73 | 15.02 | -10.51 | 0.27
Log10(ZSD) | -5.61 | 20.72 | -18.39 | 0.52
Log10(ZSA) | -5.11 | 17.04 | -14.05 | 0.24
Log10(DS) | -4.89 | 16.30 | -10.60 | 0.26
In the table, the mean of a LSP parameter is fit with a quadratic equation
where with being the UE height in m.
The LSP is modeled as a normal distribution with mean and standard deviation ,

## Slide 12
Proposal
Proposal 1: Use UE-height dependent statistical model to generate the LSPs (ASA, ASD, ZSA, ZSD, DS, K) for UAV’s fast fading modeling in UMa-AV scenario

## Slide 13
Proposal
LSP |  |  |  | 
Log10(ASD) | -0.96 | 2.54 | -0.45 | 0.38
Log10(ASA) | 0.00 | -1.74 | 3.43 | 0.31
Log10(ZSD) | 0.55 | -1.59 | 1.58 | 0.35
Log10(ZSA) | 0.34 | -1.92 | 2.42 | 0.30
Log10(DS) | 0.21 | -2.02 | 4.93 | 0.29
K | -13.43 | 62.81 | -56.30 | 5.76
Log10(ASD) | -0.96 | 2.54 | -0.45 | 0.38
Log10(ASA) | 0.00 | -1.74 | 3.43 | 0.31
Log10(ZSD) | 0.55 | -1.59 | 1.58 | 0.35
Log10(ZSA) | 0.34 | -1.92 | 2.42 | 0.30
Log10(DS) | 0.21 | -2.02 | 4.93 | 0.29
K | -13.43 | 62.81 | -56.30 | 5.76
Proposal 2: Regarding LoS LSP for fast fading in UMa-AV, the LoS LSP is modeled as a normal distribution with mean and standard deviation ,
where , and is the UE height in m.

## Slide 14
Proposal
Proposal 3: Regarding NLoS LSP for fast fading in UMa-AV, the NLoS LSP is modeled as a normal distribution with mean and standard deviation ,
where , and is the UE height in m.
LSP |  |  |  | 
Log10(ASD) | -3.22 | 11.01 | -7.76 | 0.38
Log10(ASA) | -4.73 | 15.02 | -10.51 | 0.27
Log10(ZSD) | -5.61 | 20.72 | -18.39 | 0.52
Log10(ZSA) | -5.11 | 17.04 | -14.05 | 0.24
Log10(DS) | -4.89 | 16.30 | -10.60 | 0.26
Log10(ASD) | -3.22 | 11.01 | -7.76 | 0.38
Log10(ASA) | -4.73 | 15.02 | -10.51 | 0.27
Log10(ZSD) | -5.61 | 20.72 | -18.39 | 0.52
Log10(ZSA) | -5.11 | 17.04 | -14.05 | 0.24
Log10(DS) | -4.89 | 16.30 | -10.60 | 0.26