## Slide 1: WF on definition of reliability
NTT DOCOMO, Ericsson
3GPP TSG RAN WG1 Meeting #90 R1-1714979
Prague, Czechia, 21th – 25th August 2017
Agenda Item: 5.2.8.4

## Slide 2: Background
Parameters | Value
Data type | Command and Control (C&C). This includes telemetry, waypoint update for autonomous UAV operation, real time piloting, identity, flight authorization, navigation database update, etc. Application Data . This includes video (streaming), images, other sensors data, etc.
Heights | Target up to 300 m AGL
Speeds | Horizontal: up to 160km/h for all the scenarios (Urban, Rural)
Latency | FFS: C&C: 50ms (one way from eNB to UAV) Application data: similar to LTE UE (ground user)
DL/UL data rate | C&C: [60-100] kbps for UL/DL Application data: up to 50 Mbps for UL
C&C Reliability | Up to 10-3 Packet Error Loss Rate
RAN2 has discussed the requirements for UAV and agreed the value on the following parameters.

## Slide 3: Background
Reliability is defined in TR38.802
Reliability
  Definition: Reliability is defined as the success probability R of transmitting X bits within L seconds, which is the time it takes to deliver a small data packet from the radio protocol layer 2/3 SDU ingress point to the radio protocol layer 2/3 SDU egress point of the radio interface, at a certain channel quality Q (e.g., coverage-edge).
  Denoted as R(L, Q, SE), where SE is the required spectral efficiency and SE=X/L/B where B (in Hz) is the user bandwidth that is allocable to one device.
  The latency bound L includes transmission latency, processing latency, retransmission latency and queuing/scheduling latency (including scheduling request and grant reception if any)
  Evaluation method: Link level simulation as start point

## Slide 4: Proposal
Reliability defined in TR38.802 with following modifications is used for evaluation of C&C traffic for aerial vehicles
  X = 1250 bytes
  L = [50] ms
    L is decided based on RAN2 agreement on UAV requirement. But it can be different from RAN2 requirement depending on the definition of latency.
  Reliability is evaluated for all the aerial UEs by system level simulation

## Slide 5: Proposal
For RAN1 system evaluation purpose, followings are assumed on latency for reliability calculation
  Aerial UE is RRC_CONNECTED
  Dynamic scheduling in UL and DL

## Slide 6: Proposal
Following latency components are considered in the system level simulation:
  DL:
    eNB processing and scheduling
    eNB transmission
    UE L1/L2 processing
  UL:
    Transmission of scheduling grant
    UE processing delay (decoding Scheduling grant + L1 encoding of data)
    UE sends UL transmission
    eNB receives and decodes the UL data
  Note: HARQ latency is considered when retransmission occurs