## Slide 1: WF on omission rules for partial Part 2 reporting
ZTE, Sanechips, Ericsson, MediaTek, Samsung, NTT DOCOMO, ASTRI, CATT, [Nokia, NSB]
3GPP TSG RAN WG1 Meeting #90bis R1-1718886
Prague, Czeck Republic, 9th – 13th October 2017
Agenda Item: 7.2.2.2

## Slide 2: Background
  For PUSCH CSI reporting, the following agreement has been reached in RAN1 NR#3:
    Separately encoded parts of a CSI report on PUSCH carrying UL-SCH have different transmission priority
      Part 1 (used to identify the number of information bits in part 2) has higher priority
        Part 1 is first included in a transmission in their entirety before part 2
      Information bits and/or channel coded bits of part 2 can be partially transmitted
        Omit CSI parameters corresponding to at least one subbands for part 2
          TBD by RAN1#90bis: if all of part 2 can be dropped as a special case
          TBD by RAN1#90bis: specify one of the following omission rules:
            Omitted subbands are determined based on a decimation ratio and/or a priority pattern used to order subband CSI (defined in specification)
            Omitted subbands are determined based on the measured subband CQI included in part 1

## Slide 3: Proposal
  For NR CSI reporting on PUSCH, Part 2 information bits of partial subbands can be omitted.
  Support the following priority rule to omit partial Part 2, where the priority level goes from high to low from Box #0 to Box #2N, and the omission granularity is one box in the following picture
    N is the number of CSI reports in one slot
    The CSI report numbers correspond to the order in the CSI report configuration
  Down-select one of the following Alts for CQI calculation in RAN1#91
    Alt 1: Subband CQI for each omitted subband is calculated assuming PMI in the nearest subband(s) with Part 2 reporting
    Alt 2: Subband CQI for each omitted subband is calculated assuming PMI in this subband
Box #0
Part 2 WB CSI for CSI report #1
Part 2 WB CSI for CSI report #2
...
Part 2 WB CSI for CSI report #N
Box #1
Part 2 SB CSI of even SBs for CSI report #1
Box #2
Part 2 SB CSI of odd SBs for CSI report #1
Box #3
Part 2 SB CSI of even SBs
for CSI report #2
Box #4
Part 2 SB CSI of odd SBs for CSI report #2
...
Box #2N-1
Part 2 SB CSI of even SBs
for CSI report #N
Box #2N
Part 2 SB CSI of odd SBs for CSI report #N
High priority
Low priority