## Slide 1: WF on SPS for feNB-IoT
NTT DOCOMO…
[Ericsson]
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, February 26th – March 2nd, 2018
Agenda item 6.2.6.1.4
R1-1803087

## Slide 2
Background
  Introduce UL SPS in feNB-IoT can reduce the signaling overhead and latency for RRC connected mode
    In SPS, one grant (DCI) can be followed by a number of NPUSCH transmissions, the signaling overhead of NPDCCH would be reduced
    The repetition time of NPDCCH and scheduling delay between NPDCCH and NPUSCH would be skipped. Then the latency could be reduced

## Slide 3
Proposal
UL SPS should be introduced in feNB-IoT in RRC connected mode
  Parameters such as periodicity, SPS C-RNTI could be configured via RRC signaling
  SPS activation/deactivation is indicated by DCI scrambled by SPS C-RNTI
    FFS on the detailed DCI design