## Slide 1: Title: Partial overlapping of PUCCH resources
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, February 26th – March 2nd, 2018
Agenda Item: 7.1.3.2.1
Source: Ericsson
Document for: Discussion and Decision
R1-1803531

## Slide 2: Partial overlap between AN and SR resources

## Slide 3: Outline
Summary of views
Purpose of discussion
Discussion points- AN and SR overlapping PUCCH resources
High level summary of design options
Note: This document is an updated version of R1-1803391.

## Slide 4: Summary of proposals (R1-1803389)
 | AN with format 0 | AN with format 1 | AN with format 2/3/4
SR with format 0 | Drop SR at least overlapped symbols: Lenovo (or AN), CATT (SR after), Intel (drop all SR when k>1), Nokia (logical OR over all K SR processes) Drop SR or AN depends on priority Panasonic Multiplexing on the AN resource CATT (SR before), Ericsson, Oppo, Intel (k=1), LGE, Panasonic Change CS of overlapping symbols on AN resource ZTE | Drop SR at least overlapped symbols: Lenovo (or AN), CATT, Ericsson (all SR is dropped), Intel (drop all SRs) Drop SR or AN depends on priority Panasonic, ZTE(drop AN hop containing overlapping symbol if SR prioritize) Multiplexing: Panasonic Bundle HARQ-ACK Oppo Change CS of overlapping symbols on AN resource ZTE | Multiplexing (jointly coding) on AN resource: Lenovo (SR before), CATT, Ericsson, Oppo, LGE, Nokia (AN PF2 and SR PF0), Panasonic, ZTE, Intel Puncture short into long: Oppo Drop SR at least overlapped symbols: Lenovo (SR after) Drop AN: Oppo (SR before) Drop SR or AN depends on priority Panasonic

## Slide 5
 | AN with format 0 | AN with format 1 | AN with format 2/3/4
SR with format 1 | Drop SR at least overlapped symbols: Lenovo (or AN), CATT (SR before), Intel (drop all SR when k>1) Multiplexing on the AN resource Ericsson, Oppo (SR after), Intel (k=1), LGE Multiplexing on the SR resource CATT(SR after), Drop AN: Oppo (SR before) Change CS of overlapping symbols on SR resource ZTE | Drop SR at least overlapped symbols: Lenovo (or AN),CATT (SR before), Ericsson (not fully contained), Intel (drop all SRs) Drop SR or AN depends on priority Panasonic, ZTE(drop SR hop containing overlapping symbol if SR prioritize) Multiplexing on the AN resource Erisson ( SR is fully contained), Panasonic Multiplexing on the SR resource CATT(SR after), Channel selection (similar to LTE): Oppo, LGE | Multiplexing (jointly coding) on AN resource: Lenovo (SR before), CATT, Ericsson, Oppo, LGE, Nokia (AN PF2 and SR PF0), Panasonic, ZTE, Intel Puncture short into long: Oppo Drop SR at least overlapped symbols: Lenovo (SR after) Drop AN: Oppo (SR before) Drop SR or AN depends on priority Panasonic

## Slide 6: Purpose of discussion
Proposals for multiplexing AN and SR, as well as AN/SR and CSI vary a lot. It is difficult to make any progress.
It is important to focus what it is feasible in Rel-15 and have a proper design accordingly.
  That requires reasonable compromises form all parties.
  The short coming should be addressed in Rel-16.

## Slide 7: Discussion points AN and SR overlapping PUCCH resources
Observation 1:
  For prioritization of an SR transmission over HARQ-ACK transmission, the UE should be able to determine whether the HARQ-ACK bits correspond to a high priority scheduled DL transmission.
Observation 2:
  In TS 38.321 section 5.4.4 the UE picks a SR resource (i.e. a PUCCH resource) based on which LCH received data. It is possible to configure very few logical channels so each logical channel has its own PUCCH resources, but it is a corner case and not something the PHY should rely on. Hence, the PHY does not know which LCH triggered the SR/has data.
  It is up to UE implementation if the PHY know which LCH triggered the SR/has data. Hence, we can not assume the information from PHY to MAC is exchanged.

## Slide 8: Discussion points AN and SR overlapping PUCCH resources
Observation 3:
  There is strong concern from UE vendors and some NW vendors to support a short PUCCH transmission interrupting a long PUSCH transmission duration.

## Slide 9: High level summary of design options
Three following options are identified.
Option 1: UE assumes there is no information with respect to Mac/Phy layer priority for the UCI transmission on PUCCH.
  FFS design
Option 2: UE assumes there is information with respect to PHY layer priority for the UCI transmission on PUCCH.
  FFS details (priority rules and design)
Option 3:UE assumes there is information with respect to Mac layer priority for the UCI transmission on PUCCH.
  FFS how to determine the priority rules (RAN2 input is needed)
  FFS on how to transmit PUCCH
Potential way forward:
  The design of option 1 is the simplest one with respect on not relying on RAN2 or defining new priority rules. It can be considered as a starting points while progressing on the other options if possible.

## Slide 10: Solutions for Option 1 -illustration
Case 1: AN with PUCCH F0/2/3/4 and SR with PUCCH F0/F1
Alt 1 | Alt2 (positive SR) | Alt 2 (negative SR)
AN
SR
AN/SR
AN
SR
SR
AN
SR
AN
AN
SR
AN/SR
AN
SR
AN
SR
AN/SR
AN/SR
SR starts before AN
SR starts with/after AN

## Slide 11: Solutions for Option 1 -illustration
Case 2: AN with PUCCH F1 and SR with PUCCH F0/F1
Alt 1 | Alt 2 (positive SR) | Alt 2 (negative SR)
AN
SR
AN
AN
SR
SR
AN
SR
AN
AN
SR
AN
AN
SR
AN
SR
AN
AN
SR starts before AN
SR starts with/after AN

## Slide 12: Solution for Option 1 - proposal
When a UE assumes there is no information with respect to MAC/PHY layer priority for the UCI transmission on PUCCH(select one of the following alternatives)
  When the PUCCH resource for AN with F0/F2/F3/F4 resource overlap with the PUCCH resource for SR with F1/F0:
    If SR starts after AN, AN/SR is transmitted on the AN PUCCH resource, similar to the PUCCH resources overlapping case with the same starting and ending symbols.
    If SR starts before AN,
      Alt 1: AN/SR is transmitted on the AN PUCCH resource, similar to the PUCCH resources overlapping case with the same starting and ending symbols.
      Alt 2: SR is transmitted in case of positive SR and AN is dropped. In case of negative SR, AN is transmitted.
  When the PUCCH resource for AN with F1 resource overlap with the PUCCH resource for SR with F1/F0 with different starting and/or ending symbols:
    Alt 1: Only AN is transmitted and the SR is dropped.
    Alt 2: SR is transmitted in case of positive SR and AN is dropped. In case of negative SR, AN is transmitted.

## Slide 13: Solution for Option 2 - proposal
PHY-layer priority based on SR periodicity
  When SR periodicity is shorter than duration of PUCCH resource for HARQ-ACK, the HACK-ACK transmission is stopped/dropped
  Otherwise, SR transmission is dropped
Note: Using option 2, low latency SR is not impacted

## Slide 14: Solution for Option 2 - proposal
Example (SR periodicity of 2 symbols and AN with 4 symbols)
SR is positive before 2nd SR occasion
  (what are the restriction on timing?)
SR is negative
AN
SR
SR
SR
AN
SR
SR
SR
AN
SR

## Slide 15: Recommendation based on offline discussion
Based on the offline discussion, in order to make progress, it is recommended to focus on option 1 and option 2 in general.
  In order to address the concern with respect to UE implementations and the time lime related complexity, in option 1 it is recommended to consider Alt 2.
    The revised Option 1 is captured as proposal 1 (highlighted blue).
  In order to address the concern for low latency transmission, the supportive companies for option 2 compromised to simplify that as limiting to only 2 symbol periodicity case, and combine it with option 1.
    The revised merged option 1/option 2 is captured as proposal 2 (the proposal 1 is highlighted blue).

## Slide 16: Proposal 1 (Option 1)
When the PUCCH resource for AN partially overlaps with the PUCCH resource for SR:
  If starting symbol of SR PUCCH resource is before the starting symbol of AN PUCCH resource
    If SR is positive, by the time the UE starts preparing the PUCCH, the UE transmits only SR in the SR PUCCH resource and does not transmit AN in the AN PUCCH resource.
    Otherwise, if SR is negative, the UE transmits AN in the AN PUCCH resource.
  Otherwise, if the starting symbol of the AN PUCCH resource is before the starting symbol of the SR PUCCH resource
    If AN PUCCH resource is F0/F2/F3/F4 by the time the UE starts preparing the PUCCH, the UE transmits AN and SR (positive or negative) based on the AN PUCCH resource, using the agreed AN/SR multiplexing methods for the AN and SR PUCCH resources with the same starting and ending symbols.
    If AN PUCCH resource is F1 and AN and SR have different starting and/or ending symbols, the UE transmits only AN in the AN PUCCH resource.

## Slide 17: Proposal 2 (compromised Option1/option 2)
When the PUCCH resource for AN partially overlaps with the PUCCH resource for SR:
  If the SR is configured with a periodicity of 2 symbols per slot,
    if SR is positive, the UE transmits only SR in the first possible SR PUCCH resource and stops AN transmission if it has already started. Otherwise the AN is transmitted on the AN PUCCH resource.
  Otherwise,
    if starting symbol of SR PUCCH resource is before the starting symbol of AN PUCCH resource
      If SR is positive, by the time the UE starts preparing the PUCCH, the UE transmits only SR in the SR PUCCH resource and does not transmit AN in the AN PUCCH resource.
      Otherwise, if SR is negative, the UE transmits AN in the AN PUCCH resource.
    Otherwise, if the starting symbol of the AN PUCCH resource is before the starting symbol of the SR PUCCH resource
      If AN PUCCH resource is F0/F2/F3/F4 by the time the UE starts preparing the PUCCH, the UE transmits AN and SR (positive or negative) based on the AN PUCCH resource, using the agreed AN/SR multiplexing methods for the AN and SR PUCCH resources with the same starting and ending symbols.
      If AN PUCCH resource is F1 and AN and SR have different starting and/or ending symbols, the UE transmits only AN in the AN PUCCH resource.

## Slide 18: Partial overlap between AN and CSI resources

## Slide 19: AN and SR with the same starting point
TS 38.213 Section 9.2.5.1
If a UE has periodic/semi-persistent CSI reports to transmit in a PUCCH and the UE determines a PUCCH format 2 to transmit HARQ-ACK/SR and PUCCH-F2-simultaneous-HARQ-ACK-CSI = TRUE
If a UE has HARQ-ACK in response to a PDSCH reception with a corresponding PDCCH and N_CSI^total periodic/semi-persistent CSI reports to transmit in a PUCCH and the UE determines either a PUCCH format 3 or a PUCCH format 4 to transmit HARQ-ACK/SR, and PUCCH-F3-simultaneous-HARQ-ACK-CSI = TRUE, or PUCCH-F4-simultaneous-HARQ-ACK-CSI = TRUE, respectively

## Slide 20: TS 38.212 Section 6.3.1.4.1
UCI(s) for transmission on a PUCCH | UCI for encoding | Value of
HARQ-ACK | HARQ-ACK | 
HARQ-ACK, SR | HARQ-ACK, SR | 
CSI (CSI not of two parts) | CSI | 
HARQ-ACK, CSI (CSI not of two parts) | HARQ-ACK, CSI | 
HARQ-ACK, SR, CSI (CSI not of two parts) | HARQ-ACK, SR, CSI | 
CSI (CSI of two parts) | CSI part 1 | 
 | CSI part 2 | 
HARQ-ACK, CSI (CSI of two parts) | HARQ-ACK, CSI part 1 | 
 | CSI part 2 | 
HARQ-ACK, SR, CSI (CSI of two parts) | HARQ-ACK, SR, CSI part 1 | 
 | CSI part 2 | 
Table 6.3.1.4.1-1: Rate matching output sequence length

## Slide 21: Encoding of AN/SR and CSI (TS 38.212)
 | AN/SR +CSI PUCCH resource F2 | AN/SR +CSI PUCCH resource F3/F4
CSI1, CSI2 CSI is configured with F3/F4 | FFS | Covered in spec
CSI (only one part) CSI is configured with F2 | Covered in spec | FFS

## Slide 22: Proposal 1 (offline consensus)
When AN/SR and CSI PUCCH resources have the same starting symbols, one PUCCH resource is used for transmission of AN/SR and CSI.
    If the UE is configured with more than one PUCCH resource sets, the PUCCH resource set is determined based on the total number of AN/SR and CSI. The PUCCH resource is determined based on ARI.
      FFS on UE assumption on the CSI part 2 is present
      FFS if/how to multiplex CSI and AN/SR in case PUCCH format indicated by ARI for AN/SR and CSI is different from the configured PUCCH format for CSI.
    If the UE is configured with only one PUCCH resource set,
      FSS how to determine the PUCCH resource for transmission of UCI
AN
CSI
AN
CSI
AN
CSI

## Slide 23: Proposal 2 (no offline consensus)
When AN/SR and CSI PUCCH resources have different starting symbols, the PUCCH resource with earlier starting symbol is used for transmission of its UCI (AN/SR or CSI) and the other one is dropped.
AN
CSI
AN
CSI

## Slide 24: Proposal or Clarification
When AN and SR and CSI PUCCH resources overlap, to determine the PUCCH resource for transmission of AN/SR and CSI
  Overlapping PUCCH resources of AN and SR is considered to determine the PUCCH resource for AN/SR.
  The PUCCH resource for AN/SR is considered to determined the PUCCH resource for AN/SR and CSI.