## Slide 1: Summary on CA aspects
Samsung
R1-1807699
3GPP TSG RAN WG1#93
Busan, Korea, May 21 – 25, 2018
Agenda item 7.1.3.4.2

## Slide 2: Semi-static HARQ-ACK Codebook
For PDSCH with slot aggregation over R slots
  Alt1: Determine HARQ-ACK codebook size by non-overlapped PDSCH occasions in association set - HARQ-ACK codebook is compressed to ceil(N/R) where N is the number of available slots in HARQ association set (R1-1806073, R1-1806301, R1-1806525, R1-1806630, R1-1806838)
    E.g.: Step 1: Find PDSCH candidate C1 having earliest end slot index among set of PDSCH candidates, and go to 2. Step 2: Find PDSCH candidate(s) C2 overlapping with C1 and allocate same HARQ-ACK bit for C1 and C2. step 3: Update set of PDSCH candidates by excluding C1 and C2, and go to Step 1.
  Alt2: Keep current specifications and include that number of slots can be >1 (R1-1806144, R1-1806740)
  Alt3: Keep current specifications by mapping HARQ-ACK bit for TB in each corresponding PDSCH occasion (R1-1806344, R1-1807241)
Determine PDSCH reception occasions per slot by pdsch-symbolAllocation table for DCI formats in USS - PDSCH reception occasions for PDSCHs scheduled by DCI formats in CSS are a subset of the ones for PDSCHs scheduled by DCI formats in a USS (R1-1806740)

## Slide 3: Semi-static HARQ-ACK Codebook
Exclude PDSCH candidates with time duration between last symbol and first symbol of PUCCH/PUSCH for HARQ-ACK smaller than the PDSCH processing time (R1-1807236, R1-1807067)
HARQ-ACK bits for PDSCHs scheduled by respective PDCCHs received after an UL grant scheduling PUSCH (for UCI on PUSCH) are set to NACK to maintain HARQ-ACK codebook size (R1-1807262)
To capture in TS 38.213 that “A UE is not expected to have HARQ-ACK bits to multiplex due to DCI that is no earlier by N2 symbols than current PUCCH resource” (R1-1806776)

## Slide 4: Semi-static HARQ-ACK Codebook
UE reports a PDSCH detection outcome (ACK/NACK) for a PDSCH occasion only in HARQ-ACK codebook indicated by PDSCH-to-HARQ timing field in corresponding DL DCI – UE reports NACK/DTX in other HARQ-ACK codebooks where UE reports HARQ-ACK for the PDSCH occasion
  Yes: R1-1805895, R1-1806144, R1-1806740, R1-1806838
  No (UE reports actual HARQ-ACK in each corresponding codebook): R1-1807415
  No – also, UE reports NACK in PUCCH corresponding to larger k1 than indicated k1 in DL DCI (R1-1807399)
Reconsider inclusion of PDCCH monitoring occasions for determining HARQ-ACK codebook size (R1-1806740)

## Slide 5: Miscellaneous Aspects
Support simultaneous configuration of EN-DC and CA with two PUCCH-groups in Rel-15 (R1-1807067)
  To be discussed under UE features and in the main session
A UE may assume that synchronization and RSRP/RSRQ for a SCell without SS/PBCH block and without CSI-RS configured for RSRP/RSRQ measurements is are same as for the PCell or a respective SCell with SS/PBCH block (R1-1806776)
  To be discussed in the RRM session
Prioritize grant-based PUSCH over grant-free PUSCH for UCI multiplexing (R1-1806073, R1-1806630, R1-1806838, and Docomo)
  The PUSCHs are on different cells
Prioritize earlier PUSCH over later PUSCH for UCI multiplexing (R1-1806838). Also prioritize the earlier of a PUCCH or PUSCH for UCI multiplexing (R1-1806525)
  Overlaps with UL control A.I.
For paired or unpaired spectrum and for semi-static or dynamic HARQ-ACK codebook, UE can transmit on PUSCH the HARQ-ACK corresponding to PDSCH reception(s) before UL/DL BWP switching (R1-1806301)
  No offline consensus to support – treat similar to PUCCH and drop HARQ-ACK for PDSCH received prior to BWP switching.

## Slide 6: Miscellaneous Aspects
Consider total DAI, in addition to counter DAI, in determining number of missed scheduled TBs or CBGs (for CA operation and when UE last detects DCI format 1_1) (R1-1807262)
  Offline consensus is to include, when applicable, use of total DAI in determining missed scheduled TBs or CBGs
Clarify that TB-level HARQ-ACK always applies for SPS PDSCH (including in cells with CBG-based retransmission) (R1-1806630)
  Check whether it is needed to add a sentence in the specs such as “Only TB-level HARQ-ACK is supported for SPS PDSCH”
Clarify that “last DCI format” is among the DCI formats indicating the same slot for HARQ-ACK feedback for the Dec. 2017 drop (R1-1807067)
  Offline consensus is to update 38.213 with the clarification suggested in R1-1807067 “among the DCI formats 1_0 or DCI formats 1_1 indicating the same slot for HARQ-ACK reporting”
Support of 2 PUCCH transmissions in a slot for (different) HARQ-ACK (R1-1807067, R1-1806301)
  Overlaps with URLLC related topics
For a UE with capability and configured to simultaneously receive PDSCH with DMRS Type A and with DMRS Type B in a slot, append HARQ-ACK codebook for DMRS Type B to HARQ-ACK codebook for DMRS Type A (R1-1806144)

## Slide 7: Cross-Carrier scheduling for different numerologies
The following is to be discussed under the scheduling/HARQ AI (7.1.3.3.2)
Restrict cross-CC scheduling realizations to contain UE complexity (R1-1806776)
  Alt 1: No support of cross-carrier scheduling in Rel-15.
  Alt 2: No support of cross-carrier scheduling across different numerologies in Rel-15
  Alt 3. Divided the UE feature 6-10 cross carrier scheduling into cross-carrier scheduling with same numerology (6-10a) and cross-carrier scheduling across same or different numerologies (6-10b)
  Alt 4. For cross-carrier scheduling across different numerologies, K0=0 and K2=0 are defined as first slot that is overlapped with slot of scheduling PDCCH transmission and constraints K0>X and K2>Y are defined

## Slide 8: Clarifications to confirm for cross-carrier scheduling
The following is to be discussed under the scheduling/HARQ AI (7.1.3.3.2)
Cross carrier slot-based scheduling is allowed toward same or later slot only
  Slot timing is defined by the start of the slot
When larger SCS schedules smaller SCS, overlapping slot is considered as K0=0 or K2=0
When smaller SCS schedules larger SCS, K0=0 or K2=0 is defined for slot with boundary aligned with that of slot containing the corresponding PDCCH
  Slot timing is defined by the start of the slot
When HARQ-ACK is transmitted on a carrier with smaller SCS, overlapping slot is considered as K1=0
When A/N is transmitted on a carrier with larger SCS, K1=0 is defined for slot with end boundary aligned with that of slot for the corresponding PDSCH

## Slide 9: References