## Slide 1: SLS Study on Realization of Stringent Reliability in Mode-4 NR-V2X
3GPP TSG-RAN WG1 Meeting#94
Gothenburg, Sweden, 20th - 24th August 2018
R1-1808294

## Slide 2: Introduction
In RAN #80 meeting, the new SID NR-V2X has been agreed with the objective 1 [1], as follows
1: Sidelink design [RAN1, RAN2]:
Identify technical solutions for a NR sidelink design to meet the requirements of advanced V2X services, including
  Study the support of sidelink unicast, sidelink groupcast and sidelink broadcast
  Study NR sidelink physical layer structures and procedure(s)
  Study sidelink synchronization mechanism
  Study sidelink resource allocation mechanism (also including objective 3)
  Study sidelink L2/L3 protocols
Use case groups in NR-V2X
  Vehicle platooning, advanced driving, extended sensors, and remote driving
  Stringent requirements: the maximum end-to-end latency of 3-10ms, the reliability of 99.99-99.999%, the packet size up to 60000 bytes
Study the realization issue on mode-4 based NR-V2X with the stringent reliability, under the condition of out of cellular coverage

## Slide 3: SLS based Analysis
Conventional mode-4 based sidelink transmission scheme (denoted non-orthogonal scheme) considers physical sidelink control channel (PSCCH) decoding and physical sidelink shared channel (PSSCH)-RSRP measurement
Orthogonal mode-4 based sidelink transmission scheme (denoted orthogonal scheme) considers artificially keeping the orthogonality for both PSCCH and PSSCH
  This scheme is not realistic, but it is worthwhile evaluating the best performance as the reference, so as to find out a potential solution or mechanism
Channel models in SLS
  Old channel model based on the definitions in TR 36.885
  New channel model based on the definitions in TR 37.885
Subchannelization schemes
  PSCCH mapped on to 2RBs, and PSSCH on to either 20RBs or 40RBs

## Slide 4: PRR vs. V-to-V Distance with Old Model
Orthogonal scheme can completely guarantee PRR within the vehicle-to-vehicle distance of 200m

## Slide 5: PRR vs. V-to-V Distance with New Model
Orthogonal scheme can fully guarantee PRR

## Slide 6: Observation and Proposal
Observation: In sidelinke mode-4 transmission, unlike the non-orthogonal resource selection scheme, the orthogonal resource selection scheme can achieve the stringent PRR requirement.
Proposal: Study a new potential mode-4 based resource selection mechanism, in consideration of the orthogonality between sidelink channels.