## Slide 1: 3GPP TSG RAN WG1 Meeting #99 Reno, USA, 18th – 22nd November, 2019 Agenda Item: 7.2.14 Document for: Discussion and Decision
TEI proposal on aperiodic SRS triggering
Source: ZTE, Sanechips, CMCC, OPPO
R1-1911935

## Slide 2: Issue description
A-SRS can be either triggered with DCI format 1_1 or DCI format 0_1 with UL-SCH=1 or with UL-SCH=0 and with non-zero CSI request
  NW cannot trigger SRS without DL/UL data and without CSI request due to the following restriction in current specification
TS 38.212
7.3.1.1.2 Format 0_1
  UL-SCH indicator – 1 bit. A value of "1" indicates UL-SCH shall be transmitted on the PUSCH and a value of "0" indicates UL-SCH shall not be transmitted on the PUSCH. Except for DCI format 0_1 with CRC scrambled by SP-CSI-RNTI, a UE is not expected to receive a DCI format 0_1 with UL-SCH indicator of "0" and CSI request of all zero(s)

## Slide 3: Proposal
  A-SRS can be triggered with DCI format 0_1 with UL-SCH=0 and without CSI request.
TP recommendation for TS 38.212
7.3.1.1.2 Format 0_1
<Unchanged parts are omitted>
  < Unchanged parts are omitted >
  UL-SCH indicator – 1 bit. A value of "1" indicates UL-SCH shall be transmitted on the PUSCH and a value of "0" indicates UL-SCH shall not be transmitted on the PUSCH. Except for DCI format 0_1 with CRC scrambled by SP-CSI-RNTI, a UE is not expected to receive a DCI format 0_1 with UL-SCH indicator of "0" and CSI request of all zero(s) and SRS request of all zero(s).
  <Unchanged parts are omitted>

## Slide 4: Thank you