## Slide 1: WF on SRS Transmission for NR
Samsung, Nokia, ASB, InterDigital, NTT DOCOMO, KDDI, Huawei, HiSilicon, Sony
3GPP TSG RAN WG1 Meeting NR Ad Hoc
Spokane, USA 16th - 20th Jan. 2017
Agenda item: 5.1.2.3.4
R1-1701437

## Slide 2: Background
The following was agreed in RAN1#86bis:
  NR supports aperiodic SRS transmission triggered by the network
    FFS on other trigger mechanism, e.g. event triggered
    FFS on multi-shot SRS transmission, e.g. the UE transmits SRS multiple times with single trigger from network
  FFS: NR supports at least one of followings
    Periodic SRS transmission
    Semi-persistent SRS transmission
The following was agreed in RAN1 #87:
  An NR-SRS resource comprises of a set of resource elements (RE) within a time duration/frequency span and N antenna ports (N ≥ 1)
    FFS on the time duration/frequency span
  A UE can be configured with K ≥ 1 NR-SRS resources
    Consider the maximum value of K to be a UE capability to avoid mandatory support for large values of K

## Slide 3: Proposal
NR supports periodic and semi-persistent NR-SRS transmission.
  Note aperiodic SRS transmission has been agreed
Out of K ≥ 1 configured NR-SRS resources:
  For aperiodic transmission, the UE can be configured to transmit a subset of or all K NR-SRS resources in a sweeping or non-sweeping manner.
  For periodic and semi-persistent transmission, the UE can be configured to transmit K NR-SRS resources in a sweeping or non-sweeping manner.
NR supports configurable timing of NR-SRS transmission.
NR supports SRS transmission including
  Number of SRS ports are 1,2, 4 and 8.
  Comb levels are 2 and 4
  Frequency hopping
Clarify the following agreed configurations are applicable to each NR-SRS resource from K configured NR-SRS resources:
  NR-SRS bandwidth
  Number of CP-OFDM/DFT-S-OFDM symbols
  Number of SRS ports
  Comb level