## Slide 1: WF on Rate Matching for LDPC Codes
Ericsson, Qualcomm, Intel, LG, Samsung, ZTE, MediaTek, Nokia, ASB, InterDigital
R1-1701465
3GPP TSG RAN WG1 Meeting NR Ad hoc
Spokane, USA ,16th - 20th January 2017
Agenda item 5.1.5.1

## Slide 2: Background
Agreement (RAN1#87):
UL eMBB data channels:
  Working Assumption to adopt flexible LDPC as the single channel coding scheme for small block sizes (to be confirmed unless significant issues are identified by the RAN1 Jan adhoc in relation to performance, implementation complexity and flexibility)
  (Note that it is already agreed to adopt LDPC for large block sizes)
DL eMBB data channels:
  Adopt flexible LDPC as the single channel coding scheme for all block sizes

## Slide 3: Proposal: Puncture Systematic Bits
Built-in puncturing of systematic bits is supported for LDPC coding, that is:
  At least for the initial transmission, the coded bits are taken after skipping the first Nsys,punct systematic bits
Nsys,punct is selected from: 0, Z, and 2*Z

## Slide 4: Proposal: CBRM, LBRM
The rate matching for LDPC code is circular buffer based (same concept as in LTE)
  The circular buffer is filled with an ordered sequence of systematic bits and parity bits
    FFS: Order of the bits in the circular buffer
  For IR-HARQ, each Redundancy Version (RV), RVi, is assigned a starting bit location Si on the circular buffer
  For IR retransmission of RVi, the coded bits are read out sequentially from the circular buffer, starting with the bit location Si
At the receiver, limited buffer rate matching (LBRM) is supported