## Slide 1: 4-step CBRA Procedure
gNB
UE
Msg.1
RAR
(scrambled by
RA-RNTI)
Msg.3
Msg.4
(scrambled by TC-RNTI)
HARQ-ACK
on PUCCH
ACK
CBRA succeed (Contention Resolution successful): if Msg.4 is decoded successfully, and the UE Contention Resolution Identity in Msg.4 matches the CCCH SDU transmitted in Msg3.
C-RNTI is set as the value of TC-RNTI
IDLE UE
gNB
UE
Msg.1
RAR
(scrambled by RA-RNTI)
Msg.3
Msg.4
(scrambled by C-RNTI)
UL grant for a new TX
CBRA succeed (Contention Resolution successful): If the PDCCH of Msg. 4 is addressed to the C-RNTI
CONNECTED UE
UE Contention Resolution Identity
Procedure of CONNECTED UE is applied for CBRA-BFR

## Slide 2: Contention resolution successful for CBRA-BFR
The TS 38.321 Section 5.1.5:
1> if notification of a reception of a PDCCH transmission of the SpCell is received from lower layers:
2> if the C-RNTI MAC CE was included in Msg3: -> RA for CONNECTED UE
3> if the Random Access procedure was initiated for SpCell beam failure recovery (as specified in clause 5.17) and the PDCCH transmission is addressed to the C-RNTI; or-> CBRA BFR for SpCell succeed
8.4 PDSCH with UE contention resolution identity (TS38.213)
When detecting a DCI format in response to a PUSCH transmission scheduled by a RAR UL grant, as described in [11, TS 38.321], or corresponding PUSCH retransmission scheduled by a DCI format 0_0 with CRC scrambled by a TC-RNTI provided in the corresponding RAR message [11, TS 38.321], the UE may assume the PDCCH carrying the DCI format has the same DM-RS antenna port quasi co-location properties, as described in [6, TS 38.214], as for a SS/PBCH block the UE used for PRACH association, as described in Subclause 8.1, regardless of whether or not the UE is provided TCI-State for the CORESET where the UE receives the PDCCH with the DCI format.
is DCI with CRC scrambled by C-RNTI which QCL with SSB for PRACH association

## Slide 3: If gNB missed reception of Msg. 3?
Re-transmission is scheduled by DCI scrambled by TC-RNTI (for both CONNECTED/IDLE UE)
  Note: before Contention resolution, gNB does not know this UE is CONNECTED UE or IDLE UE
  38.213:
8.3 PUSCH scheduled by RAR UL grant
For Msg3 PUSCH retransmissions, if any, of the transport block are scheduled by a DCI format 0_0 with CRC scrambled by a TC-RNTI provided in the corresponding RAR message [11, TS 38.321]. The UE always transmits the PUSCH scheduled by a RAR UL grant without repetitions.
8.4 PDSCH with UE contention resolution identity
When detecting a DCI format in response to a PUSCH transmission scheduled by a RAR UL grant, as described in [11, TS 38.321], or corresponding PUSCH retransmission scheduled by a DCI format 0_0 with CRC scrambled by a TC-RNTI provided in the corresponding RAR message [11, TS 38.321], the UE may assume the PDCCH carrying the DCI format has the same DM-RS antenna port quasi co-location properties, as described in [6, TS 38.214], as for a SS/PBCH block the UE used for PRACH association, as described in Subclause 8.1, regardless of whether or not the UE is provided TCI-State for the CORESET where the UE receives the PDCCH with the DCI format.