## Slide 1: Merged WFs on CSI reporting
Ericsson, Samsung, LG Electronics, LG Uplus, Huawei, HiSilicon, ZTE, KT, ITRI, Interdigital, Deutsche Telekom, China Telecom, China Unicom, AT&T, Telecom Italia, ITL, ITRI, NTT DOCOMO, Qualcomm, Nokia Networks
Agenda Item: 7.2.5.2.1 Document for: Decision
3GPP TSG-RAN WG1#80bis R1-152425
Belgrade, Serbia, 20th - 24th April 2015

## Slide 2: Scope
Goal: description of specification-based enhancements on CSI feedback
  To summarize the available schemes in the TR
Proposal: Capture the contents of this WF in the TR

## Slide 3: Possible schemes for non-precoded CSI-RS
A CSI reporting scheme is associated with codebook(s) for PMI reporting for 2-D antenna arrays and the associated CSI reporting modes
Precoding matrix/vector for CSI reporting:
  is used as the downlink transmission hypothesis for CSI calculation
Potential specification enhancement on CSI reporting:
  Scheme 1:
    PMI(s) corresponding to W1 and/or W2
      one or multiple PMIs (e.g. H-PMI and V-PMI) are reported for W1 and W2 respectively, different feedback rate and/or granularity for the multiple PMIs may or may not be used
    RI: A single RI or multiple RIs
    CQI

## Slide 4: Possible schemes for non-precoded CSI-RS
  Scheme 2:
    According to scheme 1 where further the precoding matrix W is extended from Rel.10/Rel.12 and can be described as follows:
    The two sub-matrices represent the two polarization groups
    X are matrices or vectors where columns are taken from a DFT matrix
    Alternative W1: k=k’ and l=l’
    The codebook for W2:
      Alternative 2-1: W2 correspond to a quantized co-phasing between two polarization groups in W1 and may also include column selection from W1.
      Alternative 2-2 W2 performs linear transformation to W1 per polarization, which may include beam selection, weighted linear combination of beams,
      Alternative 2-3 Distinct selection of beams per layer and/or per polarization, and quantized co-phasing between two polarization groups
  Scheme 3:
    W1 codebook contains only identity matrix
    PMI(s) corresponding to W2, RI and CQI
  Scheme 4:
    W1 is antenna port selection matrix
  Other schemes are not precluded

## Slide 5
Potential Enhancements related to beamformed CSI-RS-based schemes
UE measures one or multiple beamformed resource(s)
  A resource can be a NZP CSI-RS resource or CSI-RS port(s) [or a CSI process], or DRS.
UE may indicate selection of one or multiple resource(s)
UE feeds back CSI, e.g. PMI(s)/RI(s)/CQI and/or PMIs/RI(s), associated to the selected resource(s)
Note that the definition of terms such as CSI process, CSI-RS resource, CSI, DRS may be different enhanced from Rel-12
Examples are described in the following pages.

## Slide 6: Possible schemes for beamformed CSI-RS
Scheme 1A: Single CSI process, single NZP CSI-RS resource, codebook-based reporting
  W= W1 W2 structure of a hypothetical codebook is assumed
    W1 is transparent to the UE and thus not reported
  CSI W2 is reported:
    Alt.1: Selection of one or more beams along with quantized co-phasing between two polarization groups,
    Alt.2: No beam selection, only quantized co-phasing between two dual polarized ports,
    Alt.3: Weighted linear combination of beams and quantized co-phasing between two polarization groups
    Alt 4: Selection of one or more beams per layer and/or per polarization, and quantized co-phasing between two polarization groups
    Alt5: PMI(s) corresponding to the selected vertical beam(s) and the horizontal precoder within the selected beam
  Example: Beams (i.e. W1) are dynamic and UE specific
Scheme 1B: Single CSI process, single NZP CSI-RS resource, codebook-based reporting
  structure of a hypothetical codebook is assumed
    W1 and W2 are reported
    W1 : selection of one or more beams
    W2 : precoding matrix based on the NZP CSI-RS resource within the selected beam
Scheme 1C: Single CSI process, single NZP CSI-RS resource, port selection
  UE feeds back one CSI (e.g. index for port (or subset of ports) selection, RI/CQI, CSI based on subset of ports)
  UE reports one CSI, i.e. e.g. PMI/RI/CQI, based on selected NZP CSI-RS resource port(s)
  Example: Different ports of the NZP CSI-RS resource are beamformed differently

## Slide 7: Possible schemes for beamformed CSI-RS
Scheme 2A: Single CSI process , multiple NZP CSI-RS resources, single resource selection and reporting
  Multiple beamformed NZP CSI-RS resources are measured by the UE
  UE reports beam index (BI) of UE-preferred NZP CSI-RS resource
  UE reports one CSI, i.e. e.g. PMI/RI/CQI, based on selected NZP CSI-RS resource
  Example: Beams are static and corresponds different vertical directions, BI selects vertical beam, 1D codebook is used for feedback of horizontally placed dual polarized NZP CSI-RS antenna ports
Scheme 2B: Single CSI process , multiple NZP CSI-RS resources, multiple one or more resource selection and reporting
  Same as 2A except that UE reports BIs selecting one or more beamformed NZP CSI-RS’s
    Number of selected CSI-RS resources can dynamically change
  UE reports CSI(s), i.e. e.g. PMI(s)/RI(s)/CQI, based on selected NZP CSI-RS resources including either separate RI and PMI per beam or single CSI for all the selected beams

## Slide 8: Possible scheme for beamformed CSI-RS
Scheme 3: Multiple CSI processes with single CSI-RS resource each, process selection and reporting
  Multiple CSI processes are configured to a UE
  UE selects one or more CSI processes based on UE measurement
  CSI e.g. CQI(s)/PMI(s)/RI(s) for the selected CSI process and index of the selected CSI process(es) is reported
Scheme 4: Two step reporting: DRS selection and reporting + CSI-RS resource selection and reporting
  Multiple beamformed DRS are measured by the UE
  UE reports DRS index (DI) or CSI-RSRP of preferred DRS(s).
  Beamformed CSI-RS is UE specifically configured based upon reported DI. CSI, e.g., RI, PMI and CQI are fed back.
Other schemes are not precluded

## Slide 9: Possible schemes for hybrid CSI reporting
Scheme 1: Two step reporting: Non-precoded CSI-RS reporting + Beamformed CSI-RS selection and reporting
  Alternative 1:
    UE feedback CSI measured on non-precoded CSI-RS
    UE is configured with a beamformed CSI-RS, according to reported CSI
    Operation according to beamformed CSI reporting follows.
  Alternative 2:
    UE feedback RI measured on non-precoded CSI-RS
    UE is configured with a beamformed CSI-RS, according to RI and channel reciprocity
    Operation according to beamformed CSI reporting follows.
Other schemes are not precluded