## Slide 1: WF on DCI formats for MTC
Ericsson, Panasonic, Sony, NEC, InterDigital, Nokia Networks
R1-156175
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
Agenda item 7.2.1.2

## Slide 2: Background
Working assumption from RAN1#82:
  For unicast, DCI format for no and small repetition levels are same. (=DCI format M1)
  For unicast, DCI format for other repetition levels are same. (=DCI format M2)
  DCI format M1 size and DCI format M2 size can be different
  UE monitors only either DCI format M1 or DCI format M2
  FFS whether DCI format size for scheduling PDSCH and PUSCH are same or not
    If there are not the same, it means there will be M3 and M4 for the other link
  FFS M1 size and/or M2 size can be from the existing DCI format size(s)

## Slide 3: Proposal 1
Confirm the Working Assumption with the revised description of the same:
  Following four DCI formats are defined.
    DCI format used for scheduling PDSCH for no and small repetition levels. (=DCI format M1A)
    DCI format used for scheduling PUSCH for no and small repetition levels. (= DCI format M0A)
    DCI format used for scheduling PDSCH for other repetition levels. (= DCI format M1B)
    DCI format used for scheduling PUSCH for other repetition levels. (= DCI format M0B)
    DCI format M1A size and DCI format M1B size can be different
    DCI format M0A size and DCI format M0B size can be different
    FFS whether DCI format M1A size and DCI format M0A size are same
    FFS whether DCI format M1B size and DCI format M0B size are same
    UE monitors only either of following.
      to receive only DCI format M1A and DCI format M0A
      to receive only DCI format M1B and DCI format M0B
    FFS DCI format described here can be from the existing DCI format size(s)

## Slide 4: Proposal 2
DCI format M1A size and DCI format M0A size are targeted to be the same
DCI format M1B size and DCI format M0B size are targeted to be the same