## Slide 1: WF on Cross-subframe Channel Estimation for PDSCH
Ericsson, Panasonic, LG, Qualcomm
R1-156243
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
Agenda item 7.2.1.3

## Slide 2: Background (1)
Agreements from RAN1#81:
  Within subframes for M-PDCCH transmission for UEs operating coverage enhancements,
    Confirm working assumption with the following revised proposal
      The UE may assume the same precoder per antenna port applies at least on the same PRB for at least X subframes.
    FFS: The UE may assume the same precoder per antenna port applies on a PRG for at least X subframes.

## Slide 3: Background (2)
Agreements from RAN1#82:
When frequency hopping is configured for the PDSCH with DMRS-based transmission ,
  Same precoding matrix is assumed per antenna port at least on the same PRB for at least X consecutive subframes
  Precoding matrix may vary from one set of X subframes to another set of X subframes
  X is the number of consecutive subframes where PDSCH is transmitted in the same narrowband (excluding retuning time)
  This does not preclude dis-continuous transmission of the PDSCH
FFS: When frequency hopping is not configured for the PDSCH

## Slide 4: Proposal
When frequency hopping is NOT configured for the PDSCH with DMRS-based transmission,
  Same precoding matrix is assumed per antenna port at least on the same PRB for at least X consecutive subframes
  Precoding matrix may vary from one set of X subframes to another set of X subframes
  X is the number of consecutive subframes where PDSCH is transmitted in the same narrowband (excluding retuning time)
Value of X is signaled from network to UE