## Slide 1: WF on CSI reporting for class B with K=1
Samsung, NTT DOCOMO, Nokia Networks, CATT
3GPP TSG RAN WG1 Meeting #82bis R1-156247
Malmö, Sweden, 5th - 9th October 2015
AI: 7.2.4.3

## Slide 2: Periodic CSI reporting for class B K=1
CSI (CQI/PMI/RI) is reported on PUCCH format 2/2a/2b
Rel.12 periodic CSI reporting definitions are reused
  Both for mode 1-1 and 2-1
  When configured with W2-only feedback:
    Mode 1-1: For 2, 4, and 8-port, a single mode 1-1 without submodes with L-bit PMI where L≤4
    Mode 2-1: follows Rel.8 description
  When configured with legacy feedback:
    Mode 1-1 and 2-1 follow Rel.12 description

## Slide 3: Aperiodic CSI reporting for class B K=1
Rel.12 aperiodic CSI (CQI/PMI/RI) reporting mechanism is reused
  Reporting mode descriptions for modes 1-2, 2-2, 3-1, 3-2
  UCI mapping on PUSCH
Rel.12 aperiodic CSI triggering mechanism is reused