## Slide 1: WF for maximum TBS design
Huawei, HiSilicon, Ericsson, NTT DOCOMO, Samsung, NEC
3GPP TSG RAN WG1 Meeting #82bis R1-156347
Malmo, Sweden, 5th - 9th October, 2015
Agenda item: 7.1

## Slide 2: Background
R1-156105 Way forward on the maximum TBS handling NTT DOCOMO, Intel, Ericsson, Huawei, HiSilicon, Nokia Networks, NEC, Samsung
Agreements:
In Rel-12, introduce new ITBS (26A) for 64QAM and ITBS (33A) for 256QAM and the corresponding highest TBS values assuming 120 REs/PRB-pair for the PDSCH and targeting max. code rate of 0.931
  Target max. code rate of 0.931 can be revisited to 0.93 if any issue is identified for multi-layer transmissions
Configure new ITBS for 64QAM and 256QAM by higher layer signaling
  When configured, the corresponding TBS values should be applied to all the subframes for the UE scheduled by DCI formats 2C or 2D.
Introduce a new UE capability signaling to support the new maximum TBS
  Capability signaling applies to 64QAM and 256QAM if UE supports UE capability of 256QAM.
  RAN1 considers this feature to be optional.

## Slide 3: Proposal for TBS 26A
PRB | TBS |  |  |  |  |  |  |  |  | 
1~10 | 632 | 1288 | 1928 | 2600 | 3240 | 3880 | 4584 | 5160 | 5992 | 6456
11~20 | 7224 | 7736 | 8504 | 9144 | 9912 | 10296 | 11064 | 11832 | 12576 | 12960
21~30 | 13536 | 14112 | 15264 | 15840 | 16416 | 16992 | 17568 | 18336 | 19080 | 19848
31~40 | 20616 | 20616 | 21384 | 22152 | 22920 | 23688 | 24496 | 24496 | 25456 | 26416
41~50 | 26416 | 27376 | 27376 | 29296 | 29296 | 29296 | 30576 | 30576 | 31704 | 32856
51~60 | 32856 | 34008 | 34008 | 35160 | 36696 | 36696 | 36696 | 37888 | 37888 | 39232
61~70 | 40576 | 40576 | 40576 | 40576 | 42368 | 42368 | 43816 | 43816 | 45352 | 45352
71~80 | 45352 | 46888 | 46888 | 48936 | 48936 | 48936 | 51024 | 51024 | 51024 | 52752
81~90 | 52752 | 52752 | 55056 | 55056 | 55056 | 55056 | 57336 | 57336 | 57336 | 59256
91~100 | 59256 | 59256 | 59256 | 61664 | 61664 | 61664 | 63776 | 63776 | 63776 | 66592
101~110 | 66592 | 66592 | 66592 | 68808 | 68808 | 68808 | 71112 | 71112 | 71112 | 71112

## Slide 4: Proposal for TBS 33A
PRB | TBS |  |  |  |  |  |  |  |  | 
1~10 | 840 | 1736 | 2600 | 3496 | 4392 | 5160 | 5992 | 6968 | 7736 | 8760
11~20 | 9528 | 10296 | 11448 | 12216 | 12960 | 14112 | 14688 | 15840 | 16416 | 17568
21~30 | 18336 | 19080 | 19848 | 20616 | 22152 | 22920 | 23688 | 24496 | 25456 | 26416
31~40 | 27376 | 27376 | 29296 | 29296 | 30576 | 30576 | 31704 | 32856 | 34008 | 35160
41~50 | 35160 | 36696 | 36696 | 37888 | 39232 | 40576 | 40576 | 40576 | 42368 | 43816
51~60 | 43816 | 45352 | 45352 | 46888 | 48936 | 48936 | 48936 | 51024 | 51024 | 52752
61~70 | 52752 | 55056 | 55056 | 55056 | 57336 | 57336 | 57336 | 59256 | 59256 | 61664
71~80 | 61664 | 61664 | 63776 | 63776 | 66592 | 66592 | 66592 | 68808 | 68808 | 68808
81~90 | 71112 | 71112 | 71112 | 73712 | 75376 | 75376 | 76208 | 76208 | 78704 | 78704
91~100 | 78704 | 81176 | 81176 | 81176 | 81176 | 84760 | 84760 | 84760 | 84760 | 87936
101~110 | 87936 | 87936 | 87936 | 90816 | 90816 | 90816 | 93800 | 93800 | 93800 | 97896