## Slide 1: WF on PUSCH
Sierra Wireless, Nokia,Intel,CATT,…
R1-157502
3GPP TSG RAN WG1 Meeting #83 R1-157501
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.5

## Slide 2: Proposal #1
Rel-13 LC/CE UEs do not support PUSCH resource allocation type 1
Proposal #2
Rel 13 LC/CE UEs shall only support adaptive PUSCH HARQ
Notes: Notes:
Proposal #1 addresses Question 1: Should it be agreed that only UL resource allocation types 0 is supported (i.e. not support type 1)?
Possible Options:
Option 1: Support Type 0 only
Option 2: Support Type 0 and Type 1 only
Summary: All companies in the offline session and offline email preferred option 1
Proposal #2 addresses Question 5: Should PUSCH HARQ retransmission be adaptive or non-adaptive or both?
Working assumption: PUSCH HARQ operation for LC/CE UEs is synchronous
Summary: The offline email had no consensus. In the offline session several companies felt strongly this was an optimization which was not needed in rel 13.
WRT Question 7: Should LC/CE UE should interpret absent/non-detected PUSCH HARQ feedback as ACK?
Summary: The offline session discussion led to a conclusion that an agree was not needed because this is legacy behaviour.
This addresses Question 1 and question 4
WRT to Question 7: Should LC/CE UE should interpret absent/non-detected PUSCH HARQ feedback as ACK?
- The group decided this was not necessary as this is the legacy procedure already.

## Slide 3: Proposal #3
Replace working assumption:
  PUSCH HARQ operation for LC/CE UEs is synchronous
With
  PUSCH HARQ operation for LC/CE UEs is Asynchronous
    The UL grant shall include the HARQ number and RV number
    The UE is not expecting to receive the UL grant for re-transmission before n+4 (where n is the last SF of the PUSCH transmission)
  Note: Inform RAN2 about this decision
Notes: Notes:
Proposal 3 addresses questions 4 , 4.1, 4.2 ,4.3
RV number is not needed in UL grant. It is also not provided by legacy UL Grant either.
The TDD Config 0 issue is common between async and sync and may to be treated separately if needed.
MCS table work may need to consider RV cycling.

## Slide 4: Background #4 – How to set Z
RAN1#82bis agreement:
In case of PUSCH transmission from LC UEs and UEs operating coverage enhancement
  The redundancy version (RV) is cycled every Z subframes
    For no or small repetitions, Z=1
      FFS whether or not a TB can be mapped to X>1 subframes as a bundle
        Value of X FFS
    Otherwise, Z>1
      The scrambling sequences at least for PUSCH data are the same in the same Z subframes
      Z is not explicitly configured
      FFS the value of Z
  The RV cycling follows legacy RV cycling pattern i.e. RV {0,2,3,1}
TDD Background:
TDD Proposal is to set Z in mode B when R>12 to the # of consecutive UL SF in each Configuration
Notes: Notes:

## Slide 5: Proposal #4
When a Rel 13 LC UEs is configure to use PUSCH frequency hopping for RV cycling,
  UE in Mode A, Z=1
  UE in Mode B:
    For FDD if repeats <16 then Z=1 else Z = Ych
    For TDD if repeats <[12] then Z=1 else for a radio frame Z is:
      Uplink Configuration 0: 3
      Uplink Configuration 1: 2
      Uplink Configuration 2: 1
      Uplink Configuration 3: 3
      Uplink Configuration 4: 2
      Uplink Configuration 5: 1
      Uplink Configuration 6: 3 then 2
When a Rel 13 LC UEs is NOT configure to use PUSCH frequency hopping for RV cycling
  UE in Mode A, Z=1
  UE in Mode B:
    For FDD, If repeats<16 then Z=1 else Z=4
    For TDD, If repeats<[12] then Z=1 else for a radio frame Z is:
      Uplink Configuration 0: 3
      Uplink Configuration 1: 2
      Uplink Configuration 2: 1
      Uplink Configuration 3: 3
      Uplink Configuration 4: 2
      Uplink Configuration 5: 1
      Uplink Configuration 6: 3 then 2
Notes: Notes:

## Slide 6
Proposal #5
The rel13 LC/CE UE shall not support transmitting PUSCH and PUCCH in the same SF.
If PUSCH and PUCCH overlap occurs,
  When R=1 for both PUCCH and PUSCH, the rel13 LC/CE UE shall support multiplexing PUCCH bits with PUSCH.
  Otherwise the following prioritization rules apply:
    If PUCCH carries CSI then PUSCH is prioritized and PUCCH is dropped
    Otherwise PUCCH is prioritized and PUSCH is dropped. The affected PUSCH is then abandoned.
Proposal #6
The rel13 LC/CE UE shall not support transmitting PRACH and PUSCH/PUCCH in the same SF.
If PRACH and PUSCH/ PUCCH overlap occurs, the UE always prioritizes PRACH over PUSCH/PUCCH. The affected PUSCH/PUCCH is then abandoned (i.e. PUSCH/PUUCH is NOT restarted after the PRACH finishes)
Notes: These two proposal are mainly to handle error cases. In some cases, they only occur when a false M-PDCCH is decoded but since this can occur, especially in low SINR, many companies feel that it is worth specifying some behaviour.
Proposal#5 -> Question 2: How to handle overlapping PUSCH repetitions and PUCCH repetitions?
Possible Options:
Option 1: eNB avoids overlap (no need to specify overlap scenario)
Option 2: Overlap can occur
Option 2.1: UE prioritizes based on set rules – rules are FFS
Option 2.2: Prioritization and multiplexing
Summary: General agreement UE will not support simultaneous PUCCH and PUSCH. Several companies supported prioritization based on rules. Only 3 companies wanted to support multiplexing.
Proposal #6 -> Question 3: How to handle overlapping PUSCH/PUCCH repetitions and PRACH repetitions?
Possible Options:
Option 1: UE does not support PUSCH and PRACH Overlap or PUCCH and PRACH overlap
Option 2: No need to specify anything (eNB avoids overlap)
Option 3: PRACH has high priority.
Summary: General agreement that UE does not support simultaneous PRACH and PUCCH/PUSCH. Majority of companies support option that PRACH has higher priority.