## Slide 1: WF on Frequency Hopping Configurations
Nokia Networks, Ericsson, ALU, ASB, InterDigital, Intel, Sony, CATT, Panasonic, Sierra Wireless, MediaTek
R1-157704
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.2

## Slide 2: Proposal
Frequency hopping configuration for M-PDCCH –
  The first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset
    FFS whether the offset is UE-specific or cell-specific
M-PDCCH frequency hopping activation/deactivation is semi-statically configured by higher-layer signalling

## Slide 3: Proposal
Frequency hopping configuration for PDSCH –
  The first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset
    FFS whether the offset is UE-specific or cell-specific
Unicast PDSCH frequency hopping activation/deactivation is
  CE Mode A: dynamically indicated by DCI
  CE Mode B: semi-statically configured by higher-layer signalling

## Slide 4: Proposal
Frequency hopping configuration for PUSCH –
  PUSCH BW within the system BW for frequency hopping is configured
    Motivation is to avoid collision with PUCCH.
  The first narrowband is signaled, the other narrowband is determined using a configurable offset
    FFS whether the offset is UE-specific or cell-specific
PUSCH frequency hopping activation/deactivation is
  CE Mode A: dynamically indicated by DCI
  CE Mode B: semi-statically configured by higher-layer signalling

## Slide 5: Proposal
PRACH frequency hopping is between two frequencies
Frequency hopping configuration for PRACH –
  prach-FreqOffset is signaled, the other frequency for PRACH is determined using a configurable offset
PRACH frequency hopping activation/deactivation is included in PRACH resource configuration

## Slide 6: Proposal
PUCCH frequency hopping is symmetric to the central frequency of system bandwidth