## Slide 1: WF on categorizing candidate multiple access schemes for NR
CMCC, Huawei, HiSilicon, CATT, Intel …
3GPP TSG RAN WG1 #85 R1-165618
Nanjing, China
23th – 27th May 2016
Agenda item: 7.1.3.2
Document for decision

## Slide 2: Background
R1-163695 WF on Multiple Access for NR ZTE, Qualcomm
Observations:
Examples non-orthogonal schemes include (but not limited to):
  For UL, Multi-user shared access (MUSA) (e.g., R1-162226, ZTE)
  Resource spread multiple access (RSMA) (e.g., R1-163510, Qualcomm)
  Sparse code multiple access (SCMA) (e.g., R1-162153, Huawei)
  Pattern defined multiple access (PDMA) (e.g., R1-163383, CATT)
  Non-orthogonal coded multiple access (NCMA) (e.g., R1-162517, LG)
  Low code rate spreading (e.g., R1-162385, Intel)
  Frequency domain spreading (e.g., R1-162385, Intel)
  Non-orthogonal multiple access (NOMA) (e.g., R1-163111, docomo)
R1-163656 WF on multiple access for NR CMCC, Huawei, HiSilicon, Fujitsu, CATT, China Telecom
Agreements:
Non-orthogonal multiple access should be investigated for diversified NR usage scenarios and use cases
At least for UL mMTC, autonomous/grant-free/contention based non-orthogonal multiple access should be studied

## Slide 3: Observations
More than 10 non-orthogonal MA schemes are proposed in the contribution of RAN-1 #85.
Most proposed non-orthogonal MA schemes are Spreading based schemes.
From preliminary LLS results presented in the extensive contributions of RAN-1 #85, non-orthogonal MA has been proved to have gain over orthogonal MA, especially in overloaded transmission scenarios.

## Slide 4: Proposals
  The Non-orthogonal MA can be categorized based on their way to superpose users:
  Category 1: Spreading based (e.g., MUSA, PDMA, SCMA etc)
    Subcategories for the above categories are FFS.
  Category 2: Non-spreading based (e.g., NOMA etc)
  NR MA should support flexible selection and / or adjustment between orthogonal MA and non-orthogonal MA depending on specific conditions.

## Slide 5: Examples for categorization
  The NoMA can be categorized based on their way to superpose users,
  Category 1: Spreading based
    IDMA (R1-165021, Nokia ALU)
    IGMA (R1-163992, Samsung)
    LCRS (R1-162385, Intel)
    LDS-SVE (R1-164329, Fujitsu)
    LSSA (R1-164869, ETRI)
    MUSA (R1-164269, ZTE)
    NOCA (R1-165019, Nokia ALU)
    NCMA (R1-162517, LG)
    PDMA (R1-162306, CATT)
    SCMA (R1-162155, Huawei)
    RSMA (R1-164688, QC)
  Category 2: Non-spreading based
    NOMA (R1-163111, DCM)