## Slide 1: WF on subcarrier spacing in NR
Verizon Wireless, KT Corp., Reliance-jio, CHTTL
Samsung, Intel, Potevio, Fiberhome, IITH, CEWiT, Tejas Neworks
3GPP RAN1#85
Nanjing, China, 23 – 27 May 2016
Agenda: 7.1.4
R1-165734

## Slide 2: Background (1)
Agreement at RAN1#84bis:
For NR, it is necessary to support more than one values of subcarrier-spacing
  Values of subcarrier-spacing are derived from a particular value of subcarrier-spacing multiplied by N where N is an integer
    Alt.1: Subcarrier-spacing values include 15 kHz subcarrier-spacing (i.e., LTE based numerology)
    Alt.2: Subcarrier-spacing values include 17.5 kHz subcarrier-spacing with uniform symbol duration including CP length
    Alt.3: Subcarrier-spacing values include 17.06 kHz subcarrier-spacing with uniform symbol duration including CP length
    Alt.4: Subcarrier-spacing values 21.33 kHz
      Note: Other values are not excluded
    Note: other alternatives are not precluded
    FFS: exact value of a particular value and possible values of N
  The values of possible subcarrier-spacing will be further narrowed-down in RAN1#85
Companies are encouraged to provide detailed analysis and input the views in the following table

## Slide 3: Background (2)
Discussion on Monday (RAN1#85):
Working assumptions
  RAN1 concludes on alternative 1 (15 kHz) as the baseline design assumption for the NR numerology
  RAN1 concludes on scale factors N =2n for subcarrier spacing as the baseline design assumption for the NR numerology
Possible conclusions
  If RAN1 will find issues about above WA including following criteria, RAN1 should compare WA and “scale factors N = 2n as the baseline design assumption for the number of OFDM symbols per 1 msec” by Wednesday
    Design complexity
    Compatibility of different numerology from time domain and frequency domain
    Latency
    Multiplexing efficiency
    TTI/symbol boundary alignment
    Overhead of Normal CP
    Coexistence with NB-IoT and LTE
    Scalable set of supportable CC BW

## Slide 4: Observation (1)
  During offline discussions, there have been strong requests from some operators on NR to support different/diverse component carrier BWs
  Including 100 MHz and 200 MHz for eMBB
  It is important that subcarrier spacing support sufficient scalability/granularity

## Slide 5: Observation (2)
There has been NO contribution from proponents of 2m scaling that demonstrated that 2m scaling can achieve the aforementioned requirement
Below, we provide an example showing issues with 2m scaling for 100MHz BW
  fsc = f0 * 2m (f0 =15kHz) is not efficient in terms of resource utilization when supporting 100 MHz CC BW
 | M=1 | M=2 | M=4 | M=5 | M=4
Subcarrier spacing (kHz) | 15 | 30 | 60 | 75 | 60
Component carrier bandwidth (MHz) | 20 | 40 | 80 | 100 | 100
Total subcarrier bandwidth (MHz) | 18 (1200sc) | 36 (1200sc) | 72 (1200sc) | 90 (1200sc) | 72 (1200sc)
Guardband Ratio | 10% | 10% | 10% | 10% | 28% (Overhead)
OFDM symbol length (usec) | 66.67 | 33.33 | 16.67 | 13.33 | 16.67
No. of symbols/subframe | 14 | 14 | 14 | 14 | 14
Subframe length (ms) | 1.0 | 0.5 | 0.25 | 0.2 | 0.25
CP overhead | 6.57% | 6.57% | 6.57% | 6.57% | 6.57%
FFT Size | 2048 | 2048 | 2048 | 2048 | 2048
Sampling rate (MHz) | 30.72 | 61.44 | 122.88 | 153.6 | 122.88

## Slide 6: Proposal
Working Assumption discussed on Monday should be revisited to resolve the issues identified with 2m scaling
Take the following as the revised working assumption on subcarrier spacing:
  Working assumptions
    RAN1 concludes on alternative 1 (15 kHz) as the baseline design assumption for the NR numerology
    RAN1 concludes on scale factors N =2n for subcarrier spacing as the baseline design assumption for the NR numerology
    RAN1 should include the subcarrier spacing {75} kHz for different CC BW support

## Slide 7
Appendix

## Slide 8: Reference - 1
R1-163998 Proposed set of numerologies for NR Samsung

## Slide 9: Reference - 2
R1-164030 Evaluation of scalable numerology proposals Huawei, HiSilicon

## Slide 10: Reference - 3
R1-164249 Discussion of NR numerology CATT

## Slide 11: Reference - 4
R1-164486 Subcarrier spacing and other parameters for numerology NEC

## Slide 12: Reference - 5
R1-164559 Initial Evaluation Result for NR Numerology LG Electronics

## Slide 13: Reference - 6
R1-164590 Discussion on numerology sets Spreadtrum Communications

## Slide 14: Reference - 7
R1-165024 Flexible numerology for 5G Nokia, ALU Shanghai-Bell

## Slide 15: Reference - 8
R1-164870 Discussion on numerology for NR ETRI

## Slide 16: Reference - 9
R1-165162 On Numerology for New Radio Access Technology MediaTek Inc

## Slide 17: Reference - 10
R1-165177 Views on numerology for NR NTT DOCOMO, INC