## Slide 1: WF on further study of complexity for channel codes
3GPP TSG RAN WG1 #85 meeting
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.5.1
LG Electronics, Ericsson, Orange
R1-165741

## Slide 2
In RAN1#84bits, the following has been agreed on the support of channel coding design for 5G new radio.
  Agreements:
    Selection of 5G new RAT channel coding scheme(s) will consider,
      Performance
      Implementation complexity
      Latency (Decoding/Encoding)
      Flexibility (e.g., variable code length, code rate, HARQ (as applicable for particular scenario(s)))
Many company’s complexity metrics are based on computational complexity.
  Memory issues should be considered for implementation complexity
  For example, memory accesses substantially contribute to the power consumption
LDPC decoders are sometimes considered superior to Turbo decoder families in complexity. However, many companies did not compare implementations supporting the same numbers of information block lengths and code rates
Background

## Slide 3
Impact on the complexity should be studied taking into account following aspects:
  Memory issues should be considered for implementation complexity.
    We propose further discussion regarding how to quantify a metric of required memory size, the memory required for HARQ retransmission, and so on.
    We propose as following metrics:
      Energy efficiency(J/bit), Area efficiency(Gbps/mm2), memory size, number of memory accesses, and so on.
  FEC complexity supporting all info lengths and all code rates should be compared instead of single info length with some code rate.
Proposal