## Slide 1: WF on additional evaluation assumptions for high speed train scenario: Macro + relay around 30GHz
Mitsubishi Electric, ETRI, Ericsson, [Nokia]
3GPP TSG RAN WG1 Meeting #85 R1-165926 Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2

## Slide 2: Background 1/2
In R1-163887, option 2 alt. 2 (Macro + relay nodes) is agreed to be included in evaluation
In R1-165484, evaluation assumptions for Macro + relay nodes around 30GHz are agreed
Additional detailed evaluation parameters are needed.

## Slide 3: Background 2/2
SFN model (Option 2, Alt. 2) illustrated in R1-165484 as a reference for terminology
6m
3.38m
580m
580m
5m
1732m
BBU
BBU
BBU
RRH1
RRH2
RRH3
RRH1
RRH2
RRH3
RRH1
RRH2
RRH3
572m

## Slide 4: Proposal 1
Number of antenna elements of relay
  Relay Tx: up to 256
  Relay Rx: up to 256
Note: The antenna of the relay for RRH-to-Relay is located outside of a train

## Slide 5: Proposal 2
Number of antenna elements of RRH
  RRH Tx: up to 256
  RRH Rx: up to 256
Note: The above values are shown in TR 38.913

## Slide 6: Proposal 3
RRH and Relay power
  RRH Tx power: [30dBm] for system bandwidth ≥100MHz.
  Relay Tx power： [27dBm] for system bandwidth ≥100MHz.
Note: Relay Tx power is defined for relay-RRH uplink

## Slide 7: Proposal 4
Channel model
  5GCM, UMa(LOS) modified to [100%] LOS in 5GCM as the starting point.
Note: Other models can be considered.

## Slide 8: Proposal 5
Email discussion for remaining parameters
  Starting point is the multi antenna architecture agreed for the NR MIMO study