## Slide 1: WF on UL gaps for eMTC
Intel Corporation, Sony, Sequans Communications, Verizon, Sierra Wireless, ZTE, Ericsson, Qualcomm, AT&T, Nokia, Alcatel-Lucent Shanghai Bell, Samsung, NTT DoCoMo, SoftBank Mobile, CATT, Panasonic, NEC, KT Corporation, MediaTek, LG Electronics, Nordic Semiconductor, Spreadtrum, Nubia Technology, InterDigital, Virtuosys, Sharp, WILUS Inc.
R1-166035
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23-27, 2016
Agenda item 6.1.5

## Slide 2: Background
RAN4 LS (R1-163974):
  To RAN WG1 and to RAN WG2: RAN WG4 respectfully asks RAN WG1 to clarify the expected eMTC UE behaviour.
    Is RAN1 considering the introduction of any mechanism for maintaining frequency and timing accuracy in eMTC, for example similar to the mechanism used in NB-IoT?
Observation
  Maintaining 0.1ppm of frequency accuracy during long continuous UL transmission bursts spanning multiple seconds can be challenging and expensive for HD-FDD eMTC UEs
  However, depending on implementation, it may be possible for some UEs to maintain the 0.1ppm frequency accuracy
Note: RAN4 has agreed to the introduction of UL gaps for eMTC in R4-164658

## Slide 3: Proposal
UL compensation gaps are defined similar to Rel-13 NB-IoT for HD-FDD eMTC UEs by a gap period (X ms) and gap length (Y ms).
  The gaps are defined at least for PUSCH and possibly (to be decided by RAN4) PRACH
  From RAN1 perspective, it may be beneficial to align the values of X and Y with the maximum frequency hopping granularity
The UEs that don’t need UL compensation gaps shall be enabled to operate without UL compensation gaps implementation.
  1 bit in the capability report of the UE is used to indicate that the UE needs UL gaps.
  From RAN1 point of view, it is beneficial if the bit can also be provided as early as possible, e.g. in Msg3 or Msg5
UL compensation gaps are used for at least for Msg3 and possibly for PRACH (if gaps are supported for PRACH) during initial access regardless of the UE capability if the corresponding transmission duration exceeds X ms.
  For PRACH (if gaps are supported for PRACH), use of UL gaps may depend not only on X but also on PRACH configuration – to be determined by RAN4
During the UL gap durations, the corresponding PUSCH and PRACH (if gaps are supported for PRACH) transmissions are dropped.
Send an LS response to RAN4 and RAN2 (and cc to RAN) informing them of the above and requesting:
  RAN4 to determine the values of X and Y for eMTC UEs considering worst case coverage and whether UL compensation gaps are needed for PRACH transmissions and if so, whether the use of UL compensation gaps depends also on PRACH configurations;
  RAN2 to provide signaling support for the above capability signaling