## Slide 1: Discussions on CDM-8 for NP CSI-RS
Samsung
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.4.1.1
R1-166727

## Slide 2: Background
In 3GPP RAN1#85, following conclusion on CSI-RS for Class A CSI reporting was made
According to the conclusion above, this contribution provides Samsung’s views on CDM patterns of CSI-RS for Class A CSI reporting based on evaluation results according to various CDM patterns
Conclusion:
Further discussion till RAN1#86, especially regarding evaluating different alternatives, e.g., using OCC 2/4/8, high reuse of CSI-RS, etc.

## Slide 3: Pattern #1 & #2 & #3
CDM-8 patterns
  CSI-RS port mapping
A = {15, 16, 17, 18, 19, 20, 21, 22}
B = {23, 24, 25, 26, 27, 28, 29, 30}
C = {31, 32, 33, 34, 35, 36, 37, 38}
D = {39, 40, 41, 42, 43, 44, 45, 46}

## Slide 4: Pattern #4 & #5
CDM-4 patterns
  CSI-RS port mapping
A = {15, 16, 17, 18}
B = {19, 20, 21, 22}
C = {23, 24, 25, 26}
D = {27, 28, 29, 30}
E = {31, 32, 33, 34}
F = {35, 36, 37, 38}
G = {39, 40, 41, 42}
H = {43, 44, 45, 46}

## Slide 5: Initial LLS results
For UE mobility of 3km/h
For UE mobility of 30km/h

## Slide 6: Discussions
Observations
  With 6dB CSI-RS power boosting, CDM-8 outperforms CDM-4 in specific environments, e.g. low UE mobility and moderate SNR
  Potential gain from the pattern optimization for CDM-8 is marginal
Proposal
  Support of CDM-8 should be carefully studied under the considerations on performance gain and specification impact

## Slide 7: Simulation assumptions
Parameters (common) | Value / Comment
Transmission bandwidth | 5MHz
Channel model, UE velocity, spatial correlation | 3GPP TU channel, 3 km/h and 30 km/h, without spatial correlation
Antenna configuration | 32 Tx antennas / 2 Rx antennas
Detector | MMSE receiver
PDCCH / PDSCH configuration | 2 / 12 OFDM symbols per sub-frame
Modulation, code rates | Specification CQI based link adaptation
HARQ | Synchronous HARQ with Chase Combining (max 4 transmissions)
Number of allocated PRBs | 4 PRBs scheduled
CSI feedback | CQI/PMI/RI Mode 3-2 (Codebook-Config is set to ‘1’)
Feedback delay | 2 msec
Feedback periodicity | 5 msec
Channel estimation for demodulation | Non-ideal (Within one PRB: FD 3-tap MMSE + TD 2-tap MMSE channel estimation)
Channel estimation for CQI/PMI/RI computation | Non-ideal (5 PRB bundling: FD 5-tap MMSE)
Rank adaptation | On