## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-167965 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on CSI measurement and reporting in NR
Huawei, HiSilicon, …

## Slide 2: Background
Following WF has been agreed in RAN1#85:
  In NR multi-antenna schemes, studies on CSI acquisition framework include
    CSI reporting schemes
      Implicit CSI feedback
        Parameters indicating channel quality based on a set of transmission and receiving hypotheses associated with one particular UE, e.g. CQI, PMI, RI, CRI
      Explicit CSI feedback: for both quantized and unquantized/analog CSI feedback
        Parameters representing channel coefficients or some reduced-space representation thereof
      Reciprocity-based feedback
        For example, take into account interference and/or receiver hypothesis can be included
      Note: including aperiodic, periodic and semi-persistent, and single/wide band and sub-band feedback
      Mixed feedback is not precluded
    Interference measurement
    FFS: CSI measurement and/or reporting and/or triggering can be ‘self-contained’ in at least time domain

## Slide 3: Proposal
A unified CSI acquisition framework should be studied in NR, which shall support
  CSI measurement based on CSI-RS
  Beam measurement based on RS for beam management
  Implicit and explicit CSI feedback
  Reciprocity based CSI acquisition
The implicit CSI feedback methods should be studied in NR
  Codebook design
  Interference measurement results obtained from
    ZP CSI-RS
    NZP CSI-RS
    DMRS
  Beam measurement results
The explicit CSI feedback methods should be studied in NR
  Feedback of channel covariance matrix
    E.g. based on Kronecker-product
  Feedback of channel matrix or channel eigenvector
    E.g. based on multi-beam combination
  Both quantized and unquantized/analog feedback
Multi-level CSI measurement and reporting with the following features should be supported in NR
  Joint feedback of wideband/long-term and subband/short-term CSI
  Based on hybrid non-precoded and beamformed CSI-RS
  Joint feedback of explicit CSI and implicit CSI

## Slide 4: Proposal
At least the following CSI measurement and reporting mechanisms should be studied by NR
  Aperiodic CSI measurement and reporting
  Semi-persistent CSI measurement and reporting
Self-contained CSI triggering, measurement and reporting in a ‘time interval X’ should be studied in NR
  Note: here the definition of 'time interval X' follows the agreements in RAN1#85 meeting