## Slide 1: WF on Coding Technique for Control Channel of eMBB
Ericsson, Nokia, ASB, LG, NEC, Orange, IMT
R1-168170
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22-26 August 2016
Agenda item 8.1.4.1

## Slide 2: Observation
TBCC provides better or comparable performance than other coding techniques for the info block size in the range of 10 – 100 bits
List decoding can be applied to improve TBCC decoder performance
  Using list decoding or not is up to receiver implementation

## Slide 3: Proposal
  At least for control channel of eMBB UL and DL, tail-biting convolutional code (TBCC) is adopted as channel coding technique for NR
    FFS: enhancements to LTE TBCC
    FFS: if other coding techniques should also be included for control channel with info block size outside of 10-100 bits