## Slide 1: WF on Clarification of Grant-free Transmission for mMTC
ZTE, ZTE Microelectronics, Qualcomm, LGE, Convida, InterDigital, [Huawei], []…
3GPP TSG RAN WG1 #86 R1-168257
Gothenburg, Sweden
22nd – 26th August 2016
Agenda item: 8.1.2.2
Document for decision

## Slide 2: Background
Agreements:
Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
  A transmission from UE does not need the dynamic and explicit scheduling grant from eNB
  Multiple UEs can share the same time and frequency resources

## Slide 3: Proposals
  At least the following options for “autonomous/grant-free/contention based” UL transmission should be studied
    Opt. 1: a UE is allowed to randomly choose a code, a sequence or an interleaver pattern from a pool known to both eNB and UE beforehand.
      eNB receiver should perform blind detection for user separation, including Preamble/DMRS-based blind detection
    Opt. 2: MA signature, e.g code/sequence/interleaver or interleaver pattern, used by a UE is pre-configured by eNB
    Other options are not precluded