## Slide 1: WF on Hybrid CSI Reporting
NTT DOCOMO, KT corporation, ITL, KDDI, LG Electronics, Mitsubishi Electric, NEC, Samsung, Sharp, Softbank, Sony, Straightpath
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.4.2.2
R1-168286

## Slide 2: Background
From RAN1#85, description of mechanism 2A
For hybrid CSI with one CSI process, support CLASS B with K≥1 CSI-RS resources for the 1st eMIMO-Type and CLASS B with K=1 CSI-RS resources for the 2nd eMIMO-Type
  For the 1st eMIMO-Type, depending on the value of K
    K=1: CQI/RI are reported. In addition, i1 is reported for Rel.12 dual-stage codebooks
    K>1: two options
      Option 1: CRI is reported
      Option 2: PMI/RI for each CSI-RS resource are reported
  For the 2nd eMIMO-Type
    CQI/PMI/RI are reported

## Slide 3: Proposal
In addition to mechanism 1, specify simplified mechanism 2A as follows
For hybrid CSI with one CSI process, support CLASS B with K>1 CSI-RS resources for the 1st eMIMO-Type and CLASS B with K=1 CSI-RS resource for the 2nd eMIMO-Type
  For the 1st eMIMO-Type, two options
    Option 1: CRI (without CQI/PMI/RI) is reported
    Option 2 (only support K=2): PMI assuming RI=1 for each of the two CSI-RS resources are reported
  For the 2nd eMIMO-Type
    CQI/PMI/RI are reported
  No interdependence in CQI calculation between 1st and 2nd eMIMO-Types