## Slide 1: Way Forward on eMBMS enhancements
Qualcomm, Ericsson, BBC, EBU, Nokia, ASB, Dish, AT&T, Telstra, Fraunhofer IIS, Verizon, Telefónica, Intel
R1-168366
3GPP TSG RAN WG1 Meeting #86
Agenda item 7.2.6

## Slide 2: Proposal
  A single new numerology with a CP of 200us and core symbol duration of 800us is introduced for PMCH.
  If a carrier is operated with 100% MBSFN subframe allocation, the new CP length and legacy extended CP for 15kHz subcarrier spacing are supported
    It is understood that 100% MBSFN subframe allocation allows for subframes to be set aside for e.g. cell search.
      FFS: Any SI that may be needed on this carrier will also be broadcasted in these subframes
      In these subframes, FDM between PMCH and other channels (potentially with a different numerology) is not precluded.
    With the 100% MBSFN subframe confuguration, this carrier does not support unicast transmissions in the downlink
    This carrier can be configured without a unicast control region in a subset of the MBSFN subframes (including all of them)
      The UE is not expected to receive PMCH with legacy extended CP for 15kHz subcarrier spacing in the MBSFN subframes without unicast control region
      The UE is not expected to receive PMCH with the new CP in MBSFN subframes with unicast control region
  If a carrier is operated with less than 100% MBSFN subframe allocation, the new CP length and legacy extended CP for 15kHz subcarrier spacing are supported
    This carrier has at least subframes 0 and 5 of each radio frame as non-MBSFN subframes
      FFS: Further CRS reductions
    This carrier can be configured without unicast control region in a subset of the MBSFN subframes (including all of them)
      The UE is not expected to receive PDSCH/(E)PDCCH in the MBSFN subframes without unicast control region
      The UE is not expected to receive PMCH with numerologies other than the new CP length in the MBSFN subframes without unicast control region
      The UE is not expected to receive PMCH with the new CP length in MBSFN subframes with unicast control region

## Slide 3: Proposal
  eMBMS enhancements do not require changes to any channels and signals needed for MBMS operation except PMCH and MBSFN-RS
    FFS whether use of more REs, TTI extension and/or change in payload are needed for PBCH coverage enhancements.